## Slide 1
Hands On OpenCL 动手学 OpenCL
原作者：
Simon McIntosh-Smith
Tom Deakin
翻译：CycleUser
本文内部包含有下面两位的贡献：
Timothy G. Mattson (来自 Intel 英特尔公司)
Benedict Gaster (来自Qualcomm 高通公司)
V 1.2 – Nov 2014

## Slide 2
课程表
课程 | 练习
创建和设置 OpenCL 平台 | 安装 OpenCL
概览 OpenCL | 运行平台信息命令（platform info command）
OpenCL 重要基本概念 | 运行 Vadd 核函数（kernel）
概览 OpenCL 接口（APIs） | 链接（Chaining）多个 Vadd 核函数（kernels）
宿主角度（hosts view）理解核函数（kernels） | 解决 D = A+B+C 问题
OpenCL 核编程（kernel programming）导论 | 矩阵乘法
理解 OpenCL 内存层级（memory hierarchy） | 优化矩阵乘法
OpenCL 中的同步性（Synchronization） | 圆周率 π 计算程序
OpenCL 异构计算（Heterogeneous computing） | 在多个设备（devices）上运行核函数（kernel）
优化 OpenCL 性能 | 程序分析（Profile a program）
借助 OpenCL 开启移动性能（portable performance ） | 为跨平台（cross-platform）优化矩阵乘法
OpenCL 开发调试 | 
将 CUDA 代码移植到 OpenCL | 移植 CUDA 代码到 OpenCL
附录 | 
Notes: 2

## Slide 3
课程参考资料
除了本讲义, C++ API 头文件, 一系列的练习题和解题答案, 还建议参考下面的内容：
OpenCL 1.1 Reference Card
这个卡片很有助于记住各个API：
https://www.khronos.org/files/opencl-1-1-quick-reference-card.pdf
v1.1 版本的详细文档可读性很好，推荐日常备一本阅读:
https://www.khronos.org/registry/cl/specs/opencl-1.1.pdf
Notes: 3

## Slide 4
创建和设置 OpenCL 平台
章节 1

## Slide 5
创建和设置 OpenCL 平台 的一些注意事项
本节将包括对下面几种平台和设备上安装 OpenCL 的指南：
  AMD CPU, GPU 和 APU
  Intel CPU
  NVIDIA GPU
本文是假设你在使用 64-bit 的 Ubuntu 12.04 LTS
（翻译者使用的是 64-bit 的 Ubuntu 18.04，会在后续版本中注明旧版/新版以示区分）

## Slide 6
多种平台支持！
OpenCL 可以运行在很多平台上
为了和每个设备所用的库函数协调合作，运行环境（runtime）使用 ICD 进行区分
如果你针对通用运行环境（generic runtime）来编译代码, ICD 就会在需要的时候加载正确的平台运行环境（ platform runtime ）
这些运行环境可以在/etc/OpenCL/vendors 这个目录下找到

## Slide 7
使用 OSX?
OpenCL 已经自带了!
编译代码的时候加上下面的关键字即可：-framework OpenCL -DAPPLE

## Slide 8
AMD GPU用户的安装过程（旧版）
首先安装一些依赖包:
  sudo apt-get install build-essential linux-headers-generic debhelper dh-modaliases execstack dkms lib32gcc1 libc6-i386 opencl-headers
下载官方驱动，可以访问 amd.com/drivers
  选择好你的 GPU 型号，操作系统版本等等.
  下载.zip 文件
  解压缩下载的 zip 文件
运行下面的命令创建安装包
  sudo sh fglrx*.run --buildpkg Ubuntu/precise
安装驱动
  sudo dpkg –i fglrx*.deb
更新 Xorg.conf 文件
  sudo amdconfig --initial --adapter=all
重启!
  检查一下是不是都装好了，运行 fglrxinfo
* Fglrx 这里指代的是与你所用 AMD GPU 对应的驱动名称
译者注：安装 Ubuntu 18.04 的 AMD 用户请参考新版的安装指南
https://zhuanlan.zhihu.com/p/75605147

## Slide 9
AMD CPU用户的安装过程（旧版）
从 AMD 官网下载 AMD APP SDK
解压缩，命令大概是 tar -zxf file.tar.gz
安装
  sudo ./Install*.sh
创建库（library）和包含路径（include）的符号链接（symbolic link）sudo ln –s /opt/AMDAPP/lib/x86_64/* /usr/local/lib
  sudo ln –s /opt/AMDAPP/include/* /usr/local/include
更新链接器路径（linker paths）
  sudo ldconfig
重启然后运行 clinfo
  你的 CPU 就应该被列出了
译者注：安装 Ubuntu 18.04 的 AMD 用户请参考新版的安装指南
https://zhuanlan.zhihu.com/p/75605147

## Slide 10
AMD APU用户的安装过程（旧版）
最简单的方法就是按照 AMD GPU 的安装指南来安装 fglrx。
这意味着你可以将 APU 中的 CPU 和 GPU 作为两个独立的 OpenCL 设备来使用。
如果你安装有独立显卡，可能需要在 BIOS 里面强制启用集成显卡，才能实现利用 APU 作为 OpenCL 设备。
译者注：安装 Ubuntu 18.04 的 AMD 用户请参考新版的安装指南
https://zhuanlan.zhihu.com/p/75605147

## Slide 11
Intel CPU 用户的安装过程（旧版）
注意: 在 Linux 系统上需要英特尔至强 Intel® Xeon™ 处理器
从 Intel 官网下载 Xeon Linux SDK
解压缩下载的文件
tar -zxf download.tar.gz
安装依赖包
sudo apt-get install rpm alien libnuma1
还可以使用 alien 来安装
  sudo alien –i *base*.rpm *intel-cpu*.rpm *devel*.rpm
将 ICD 复制到正确路径下
  sudo cp /opt/intel/<version>/etc/intel64.icd /etc/OpenCL/vendors/

## Slide 12
Intel GPU 用户的安装过程（旧版）
注意: 在 macOS 系统上需要英特尔至强 Intel® Xeon™ 处理器
根本不用折腾，出场就能用!
只要选择 Intel® GPU 设备来运行 OpenCL即可
Intel® 还有专门针对 Windows 的驱动: https://software.intel.com/en-us/articles/opencl-drivers

## Slide 13
Intel® Xeon Phi™ 安装过程（旧版）
Intel® Xeon Phi™ 协处理器（coprocessor） 是一类比较特殊的处理器，一般只在超级计算机（HPC）集群（cluster）中常用到。
因此，这里就假设大多数用户都是在别人建立好的服务器环境中使用这样的设备，所以本文就不再讲解针对 Intel® Xeon Phi™ 协处理器的 OpenCL 安装过程了。

## Slide 14
NVIDIA GPU用户的安装过程（旧版）
一定要先屏蔽开源驱动！这超级重要！
  sudo nano /etc/modprobe.d/blacklist.conf
  在上面的编辑器中加上这一行: blacklist nouveau
安装依赖包
  sudo apt-get install build-essential linux-header-generic opencl-headers
从官网下载驱动然后解压缩
进入虚拟终端（快捷键 Ctrl+Alt+F1）停止桌面管理器
  sudo service lightdm stop
设置运行权限然后运行
  chmod +x *.run
  sudo ./*.run
预备安装（pre-install）可能会失败，这不要紧！
同意选择 DKMS, 32-bit GL 库（libraries） 来更新 X config
重启！

## Slide 15
安装 pyopencl
你得先保证自己安装好 Python
然后安装 numpy 库（library）
  sudo apt-get install python-numpy
从 pyopencl 官网下载最新版本
  然后解压缩 tar -zxf
运行下面的命令来安装这个包
  python setup.py install --user
译者注：现在可以直接用 pip 安装 pyopencl
  pip install pyopencl

## Slide 16
C/C++ 链接 (gcc/g++)
要编译 OpenCL 程序，你必须告诉编译器 （compiler）去使用 OpenCL 库（library），就要在编译的时候加上备注（flag）: –l OpenCL
编译器应该能找到 OpenCL 头文件（header files）了，如果找不到，你就得指定具体的 CL/ 文件夹的路径，这需要加上 –I (一定要是大写的，不能用 “i”)备注（flag）
链接器（linker）应该能找到 OpenCL 运行环境库（ runtime libraries ），如果找不到，你就得加上 –L（注意也要是大写哈）备注（flag） 来指定 lib 文件夹位置
还得确定你使用的 gcc/g++ 版本得足够新，要使用 OpenCL C++ API 要求最低也得是 v4.7 版本（因为需要支持 C++11）

## Slide 17
概览 OpenCL
章节 2

## Slide 18
这是一个异构的世界
OpenCL 允许开发者写一份可以移植的代码，在不同平台上都可以使用所有的资源。
现代的计算平台包括
一个或多个 CPU
一个或多个 GPU
DSP 处理器
加速器(accelerator)
… 其他的
例：三星® Exynos 5:
双核 ARM A15 1.7GHz, Mali T604 GPU
例： Intel XXX with IRIS

## Slide 19
微处理器的趋势
单个处理器的核心数量越来越多，这些核心还很可能是异构的。
异构（Heterogeneous）和众核（many-core）带来的挑战:
如何为这些异构众核设备构建一个软件生态系统？
第三方名称是其公司所有财产
61 cores
16 wide SIMD
NVIDIA® Tesla® C2090
10 cores
16 wide SIMD
ATI™ RV770
16 cores
32 wide SIMD
Intel® Xeon Phi™协处理器

## Slide 20
异构平台开发的工业标准
OpenCL – 开放（Open）计算语言（Computing Language）
针对异构并行计算的CPU，GPU 等设备的可移植的并行计算的开放标准，免受专利限制
CPUs
多核心驱动性能提升
GPUs
通用数据并行计算日益增加
图形 API 和着色器语言
多处理器编程 例：OpenMP
新兴交叉领域
异构计算
第三方名称是其公司所有财产

## Slide 21
OpenCL 的起源
AMD
ATI
NVIDIA
Intel
Apple
两家公司合并后需要对产品的通用支持
GPU 厂商想要抢占CPU 市场
CPU 厂商想要抢占 GPU 市场
厌倦了对不同的众核设备和 GPU 等重复开发，推动厂商们标准化
写一个草稿，稻草人（straw man）API
Khronos 计算组织成立
ARM
Nokia
IBM
Sony
Qualcomm
Imagination
TI
+ many more
第三方名称是其公司所有财产

## Slide 22
Khronos 组织内的 OpenCL 开发团队
多种厂商参与
  处理器厂商，系统设备制造商, 中间件制造商, 应用开发者。
由于这些参与者的市场覆盖范围和影响力巨大，OpenCL 一发布就成了一个重要的标准。
第三方名称是其公司所有财产

## Slide 23
OpenCL 时间线
2008年6月正式发布… 从草稿的“稻草人（StrawMan）API” 到 OpenCL 1.0 发布，用了6个月
迅速迭代以紧跟硬件发展的步伐
  从 1.0 到 1.1 ，从 1.1 到 1.2 18 个月
  既定目标: 每隔18-24 个月发布一个新版本
  致力于向后兼容以保障软件开发
Khronos 公布了OpenCL 1.0 细节参数
2009年
多个平台实现多个同样实现
2008年12月
2010年7月
Khronos 公布了正式版 OpenCL 1.1 细节参数， 不久后就可以得到实现
2011年11月
发布了 OpenCL 1.2

## Slide 24
OpenCL 时间线
OpenCL 1.0 发布并进行测试
2008年12月
2010年6月
OpenCL 1.1 发布并进行测试
2011年11月
OpenCL 1.2 发布并进行测试
2013年11月
OpenCL 2.0 最终发布并进行测试
2013年7月
OpenCL 2.0 预览版发布
2008年6月正式发布… 从草稿的“稻草人（StrawMan）API” 到 OpenCL 1.0 发布，用了6个月
迅速迭代以紧跟硬件发展的步伐
  从 1.0 到 1.1 ，从 1.1 到 1.2 18 个月
  既定目标: 每隔18-24 个月发布一个新版本
  致力于向后兼容以保障软件开发

## Slide 25
OpenCL: 从手机到超级计算机
OpenCL 嵌入式版本针对移动和嵌入式设备设计
  放宽数据类型和精度要求
  避免需要单独的 “嵌入式ES”规范
Khronos API 为图形和图像提供计算支持
  支持高级应用，比如增强现实
  OpenCL 使得新市场领域中的并行计算成为可能
  手机，汽车，航空电子设备
带有GPS的照相手机可以识别建筑物然后标记出来，并从互联网上获取相关信息

## Slide 26
OpenCL 平台模型
一个宿主（Host）以及一个或者多个 OpenCL 设备 （Device）
  每个 OpenCL 设备都由一个或者多个计算单元（Compute Units）组成，计算单元后文常缩写为 CU
    每个计算单元都可以分成一个或者多个处理元素（Processing Elements），后文缩写为 PE
内存（Memory）分为宿主内存（host memory）和设备内存（device memory）
处理元素（Processing Elements）
OpenCL 设备（Device）
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
宿主（Host）
计算单元（Compute Unites）

## Slide 27
OpenCL 平台样例 (一个节点，双路 CPU，双 GPU)
CPU:
看做一个 OpenCL 设备(device)
  每个核心（core）一个计算单元（CU）
  每个计算单元一个处理元素（PE），或者如果 PE 映射到单指令多数据流（SIMD lanes），则每个 CU 有 n 个 ，这里的 n 等同于单指令多数据流的带宽（ SIMD width ）
记住：
  CPU本身也是自己的宿主（Host）
GPU:
每个 GPU 是一个单独的 OpenCL 设备（device）
通过 OpenCL 可以同时使用 CPU 和所有 GPU 设备
CU = Compute Unit 计算单元
PE = Processing Element 处理元素

## Slide 28
练习 1: 获取平台信息
目标:
  验证一下你能够运行一个简单的 OpenCL 程序。
流程:
  利用已经提供的 DeviceInfo 程序，选用一个编辑器来阅读一下代码，然后构建并运行。
预期输出:
  应该会输出你所安装的 OpenCL 平台信息以及所有可见设备的信息。
扩展:
  运行命令 clinfo ，这个命令来自于 AMD 公司提供的 SDK，但可以运行于所有 OpenCL 平台之上。这个命令运行后你会看到 OpenCL 运行环境能找到的所有设备和平台的相关信息。

## Slide 29
OpenCL 重要基本概念
章节 3

## Slide 30
OpenCL 平台模型
一个宿主（Host）以及一个或者多个 OpenCL 设备 （Device）
  每个 OpenCL 设备都由一个或者多个计算单元（Compute Units）组成，计算单元后文常缩写为 CU
    每个计算单元都可以分成一个或者多个处理元素（Processing Elements），后文缩写为 PE
内存（Memory）分为宿主内存（host memory）和设备内存（device memory）
处理元素（Processing Elements）
OpenCL 设备（Device）
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
宿主（Host）
计算单元（Compute Unites）

## Slide 31
OpenCL 背后的大智慧
将循环替换成在一个问题域（problem domain）内每个点运行的函数(一个 核函数kernel)
  例如，处理一个 1024x1024 像素大小的图像，调用一个核函数处理每个像素点或者直接进行 1024x1024=1,048,576 次核函数运行
传统循环
OpenCL 数据并行
void
mul(const int n,
const float *a,
const float *b,
float *c)
{
int i;
for (i = 0; i < n; i++)
c[i] = a[i] * b[i];
}
__kernel void
mul(__global const float *a,
__global const float *b,
__global float *c)
{
int id = get_global_id(0);
c[id] = a[id] * b[id];
}
// 称为工作项目的
// 很多核函数的实例
// 都是并行执行的

## Slide 32
工作项（ work-items ）的N维域（ N-dimensional domain ）
全局维度（ Global Dimensions ）:
  1024x1024 (整个问题空间 problem space)
局部维度（ Local Dimensions ）:
  64x64 (工作组work-group, 一起执行)
选择对你所用算法（ algorithm ）来说“最优”的维度（dimensions）
1024
1024
只有同一个工作组 work-groups 内的工作项 work-items 才能进行同步（synchronization）:
屏障 barriers 和 内存围栏memory fences
一个核（kernel）内的工作组 work-groups 之间不能同步（ synchronize ）

## Slide 33
OpenCL 的 N 维度范围（N Dimensional Range，缩写为 NDRange)
我们要计算的问题应该具有某一个确定的维度（dimensionality）;
  假设要针对一个立方体（cube）上面的所有点计算一个核函数（kernel）
运行这个核函数（kernel）的时候就要指定最高为三维（up to 3 dimensions）
还要指定每个维度上的问题规模 （specify the total problem size ）– 这叫做全局规模（global size）。
然后将迭代空间（iteration space）中的每个点关联到一个工作项（work-item）。

## Slide 34
工作项（work-items） 划分组别就成了工作组（work-groups）; 同一个工作组内的工作项可以共享本局部内存（ local memory ）并且可以同步（synchronize）
可以指定一个工作组中的工作项的个数这个个数也叫做局部规模或者工作组规模（local (work-group) size）。
或者 OpenCL 运行环境（ run-time ）也可以为替你来设置一个工作组规模，不过通常都不是最优设置。
OpenCL 的 N 维度范围（N Dimensional Range，缩写为 NDRange)

## Slide 35
OpenCL 内存模型（ Memory model ）
私有内存 Private Memory
  每个工作项 work-item
局部内存 Local Memory
  工作组 work-group 内分享
全局内存/恒定内存Global Memory /Constant Memory
  对所有工作组都可见
宿主内存 Host memory
  在 CPU 上
内存管理是 明确的（ explicit ）: 你要负责把数据在 宿主 host → 全局 global → 局部 local 之间来回移动

## Slide 36
上下文（ Context ）和命令队列（ Command-Queues ）
上下文 （ Context ）:
  核函数运行的环境，也是同步和内存管理的定义域。
这里的 上下文 （ context ）包括:
  一个或者多个设备（ devices ）
  设备内存（ Device memory ）
  一个或者多个命令队列（ command-queues ）
一个设备的所有命令（commands） ，（例如 核函数执行 kernel execution，同步 synchronization，内存转移操作 memory transfer operations）都是通过一个命令队列（ command-queue ）来提交（ submitted ）。
每个 命令队列（command-queue） 都指向一个上下文（context）内的某一个单独的设备（device）。
命令队列
Queue
上下文Context
设备
Device
设备内存
Device Memory

## Slide 37
执行模型（核函数）
Execution model (kernels)
OpenCL 执行模型（ execution model ）… 定义一个问题域（problem domain）然后对域中每个点运行一个核函数实例（instance of a kernel）。
译者注：下面的例子就是对所有元素乘以2的一个函数的示意图。
__kernel void times_two(
__global float* input,
__global float* output)
{
int i = get_global_id(0);
output[i] = 2.0f * input[i];
}
get_global_id(0)
10
Input
Output
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 42 | 44 | 46 | 48 | 50

## Slide 38
__kernel void
horizontal_reflect(read_only image2d_t src,
write_only image2d_t dst)
{
int x = get_global_id(0); // x-coord
int y = get_global_id(1); // y-coord
int width = get_image_width(src);
float4 src_val = read_imagef(src, sampler,
(int2)(width-1-x, y));
write_imagef(dst, (int2)(x, y), src_val);
}
构建程序对象
Building Program Objects
所谓的程序对象（ program object）是对下面各项的封装（encapsulates） :
  一个上下文环境（context）
  程序核函数（kernel）的代码或者二进制文件
  目标设备（target devices）列表以及创建选项（build options）
创建程序对象的 C API 构建过程（build process）:
  clCreateProgramWithSource()
  clCreateProgramWithBinary()
OpenCL 使用的是 运行时编译 （runtime compilation）… 因为通常发送程序过去的时候你也不知道目标设备的细节。
针对 GPU 编译
针对 CPU 编译
GPU
代码
CPU
代码

## Slide 39
举例: 向量加法
学编程的一般都知道第一个程序就是所谓的“hello world”程序。对于数据并行编程来说， “hello world”程序就是将两个向量相加：
C[i] = A[i] + B[i] for i=0 to N-1
用 OpenCL 来解决，就需要写两部分代码：
  核函数代码（ Kernel code ）
  宿主代码（Host code）

## Slide 40
向量加法- 核函数 Kernel
__kernel void vadd(__global const float *a,
__global const float *b,
__global float *c)
{
int gid = get_global_id(0);
c[gid] = a[gid] + b[gid];
}

## Slide 41
向量加法– 宿主 Host
宿主程序（host program）顾名思义是运行在宿主（Host） 上的，功能是：
  设置 OpenCL 程序运行的环境
  创建和管理核函数（kernels）
一个基础的宿主程序可以划分成五个步骤：
  定义 平台（ platform ） … 平台（ platform ） = 设备 （ devices ）+ 上下文 （ context ）+ 命令队列（ queues ）
  创建 （ Create ）并构建 （ Build ）该程序 （ program ）(核函数（kernels）运行所需的动态链接库（ dynamic library ）)
  设置 内存对象（memory objects）
  定义核函数（kernel） (附加上传递给核函数的参数（arguments）)
  提交（submit）命令 commands … 转移内存对象（ transfer memory objects ） 然后执行核函数（execute kernels）
接下来的讲义中，需要交叉阅读讲义和参考卡上面的内容。这会有助于你习惯于使用参考卡，从卡片中获取信息，然后用代码来表达出来。

## Slide 42
OpenCL 中的基本平台（basic platform）和运行时环境接口（runtime API） (使用 C 语言)
arg [0] value
arg [1] value
arg [2] value
arg [0] value
arg [1] value
arg [2] value
In Order
Queue
Out of Order
Queue
GPU
上下文 Context
__kernel void
dp_mul(global const float *a,
global const float *b,
global float *c)
{
int id = get_global_id(0);
c[id] = a[id] * b[id]; }
dp_mul
CPU 程序二进制文件
dp_mul
GPU 程序二进制文件
Programs
arg[0] value
arg[1] value
arg[2] value
缓存
Buffers
图像
Images
有序队列
In Order
Queue
无序队列
Out of Order
Queue
计算设备Compute Device
GPU
CPU
dp_mul
程序
Programs
核函数
Kernels
内存对象
Memory Objects
命令队列
Command Queues
编译代码
Compile code
创建数据和参数
Create data & arguments
发送执行
Send to execution

## Slide 43
1. 定义平台（platform）
获取第一可用平台（ first available platform ）:
err = clGetPlatformIDs(1, &firstPlatformId,
&numPlatforms);
使用平台提供的第一个 CPU 设备（ device ）:
err = clGetDeviceIDs(firstPlatformId,
CL_DEVICE_TYPE_CPU, 1, &device_id, NULL);
创建一个单独设备（single device）的简单上下文环境（ simple context ）:
context = clCreateContext(firstPlatformId, 1,
&device_id, NULL, NULL, &err);
针对设备（device）创建一个简单的命令队列（ command-queue ）:
commands = clCreateCommandQueue(context, device_id,
0, &err);

## Slide 44
命令队列
Command-Queues
命令队列中的命令（command）包括：
  核函数执行（ Kernel executions ）
  内存对象管理（ Memory object management ）
  同步（Synchronization）
提交命令（commands）到一个设备（device）的唯一方式就是通过一个命令队列（command-queue）。
每个命令队列（command-queue）都指向在一个上下文环境（context）中的某个单一设备（single device。
对某个单一设备(single device)可以提供多个命令队列（Multiple command-queues）。
  这一特性可以用于定义不需要同步（synchronization）的独立命令流（ independent streams of commands）。
队列
Queue
队列
Queue
上下文环境
Context
GPU
CPU

## Slide 45
命令队列的执行细节
Command-Queue execution details
命令队列（command queues）可以配置成不同方式来控制命令如何执行
有序队列 In-order queues:
  命令进行排序然后按照他们在程序中出现的顺序进行执行 (程序顺序program-order)
无序队列 Out-of-order queues:
  命令按照程序顺序（ program-order ）排序，但执行的时候可以按照任意顺序来执行（即完成）。
命令队列内的命令执行能够确保在同步点（ synchronization points）完成
  稍后再讲
队列
Queue
队列
Queue
上下文环境
Context
GPU
CPU

## Slide 46
2. 创建并构建程序
以字符串文本（string literal）方式定义核程序（kernel-program）的源代码（很适合样例代码），或者也可以从一个文件中读取（这就是对应真实应用了）。
构建程序对象（ program object ）:
program = clCreateProgramWithSource(context, 1
(const char**) &KernelSource, NULL, &err);
编译（ Compile ）上面的程序（program）俩创建一个“动态链接 dynamic library”，可以从中提取特定的核函数（kernels）:
err = clBuildProgram(program, 0, NULL,NULL,NULL,NULL);

## Slide 47
错误信息
Error messages
获取并打印错误信息（ error messages ）:
if (err != CL_SUCCESS) {
size_t len;
char buffer[2048];
clGetProgramBuildInfo(program, device_id,
CL_PROGRAM_BUILD_LOG, sizeof(buffer), buffer, &len);
printf(“%s\n”, buffer);
}
检查你的 OpenCL API 错误信息很重要！
在 C++ 里面使用 try/catch 就更简单了（后面再说）

## Slide 48
3. 创建内存对象
对于向量加法，我们需要用到三个内存对象，分别对应着输入的向量 A 和 B,以及一个输出向量 C。
在宿主上（ on the host ）创建输入向量并且赋值 :
float h_a[LENGTH], h_b[LENGTH], h_c[LENGTH];
for (i = 0; i < length; i++) {
h_a[i] = rand() / (float)RAND_MAX;
h_b[i] = rand() / (float)RAND_MAX;
}
定义 OpenCL 内存对象（ memory objects ）:
d_a = clCreateBuffer(context, CL_MEM_READ_ONLY,
sizeof(float)*count, NULL, NULL);
d_b = clCreateBuffer(context, CL_MEM_READ_ONLY,
sizeof(float)*count, NULL, NULL);
d_c = clCreateBuffer(context, CL_MEM_WRITE_ONLY,
sizeof(float)*count, NULL, NULL);

## Slide 49
往设备内存（device memory）里面放什么?
内存对象（Memory Objects）:
一个句柄（handle），指向全局内存（global memory）中引用-计数区域（ reference-counted region）。
有两种类型的内存对象（memory object）
缓存对象（ Buffer object ）:
  定义多个字节组成的一个线性集合 (“就是一个 C 语言数组array”)。
  缓存对象的内容完全暴露在核函数（kernel）内，可以通过指针（pointer）进行读取
图像对象（ Image object ）:
  定义了内存中的一个二维或者三维的区域。
  图像数据 只能 通过 读 read 和 写 write 这两个函数来使用，也就是说，是一种不透明数据结构（ opaque data structures ）。读取函数 read 用作了取样器（sampler）。
Used when interfacing with a graphics API such as OpenGL. We won’t use image objects in this tutorial.

## Slide 50
创建并操作缓存（buffer）对象
缓存对象可以在宿主（host）上通过类型来声明（declare）: cl_mem
宿主内存（host memory）中的数组（arrays）存储了原始的宿主侧数据（host-side data）:
float h_a[LENGTH], h_b[LENGTH];
创建缓存对象（ buffer ） (d_a), 对“h_a” 进行 sizeof(float)*count ，将所得字节赋值到这个缓存对象，然后将其复制到设备内存（device memory）:
cl_mem d_a = clCreateBuffer(context,
CL_MEM_READ_ONLY | CL_MEM_COPY_HOST_PTR,
sizeof(float)*count, h_a, NULL);

## Slide 51
缓存对象的命名约定
有时候如果分不清一个宿主变量（host variable）到底是普通的 C 语言数组（array）还是一个OpenCL 缓存对象（buffer）。
对此有一个有用的办法就是约定一个前缀，常规的宿主 C 语言数组（ host C arrays ）就加上前缀“h_” ，而 OpenCL 缓存（buffer）是在设备（ device ）上的，就加上前缀 “d_”。

## Slide 52
其他常用的内存标记（memory flags）包括:
CL_MEM_WRITE_ONLY, CL_MEM_READ_WRITE
  这些是从设备（device）视角出发的。
然后提交命令将缓存对象（buffer）复制回宿主内存（host memory）的 “h_c” 位置:
  CL_TRUE = 阻塞（blocking）,
  CL_FALSE = 非阻塞（non-blocking）
clEnqueueReadBuffer(queue, d_c, CL_TRUE,
sizeof(float)*count, h_c,
NULL, NULL, NULL);
创建并操作缓存（buffer）对象

## Slide 53
4. 定义核函数（kernel）
从核函数（kernel function） “vadd” 创建 核对象（kernel object）:
kernel = clCreateKernel(program, “vadd”, &err);
附加核函数“vadd”的参数到内存对象（memory objects）:
err = clSetKernelArg(kernel, 0, sizeof(cl_mem), &d_a);
err |= clSetKernelArg(kernel, 1, sizeof(cl_mem), &d_b);
err |= clSetKernelArg(kernel, 2, sizeof(cl_mem), &d_c);
err |= clSetKernelArg(kernel, 3, sizeof(unsigned int), &count);

## Slide 54
5. 命令排序（ Enqueue commands ）
将缓存（ Buffers ） 从宿主写到全局内存 （ global memory ）(作为非阻塞操作（ non-blocking operations ）):
err = clEnqueueWriteBuffer(commands, d_a, CL_FALSE,
0, sizeof(float)*count, h_a, 0, NULL, NULL);
err = clEnqueueWriteBuffer(commands, d_b, CL_FALSE,
0, sizeof(float)*count, h_b, 0, NULL, NULL);
将核函数（kernel）排序等待执行（execution） (注意: 这里用有序队列（ in-order queue）):
err = clEnqueueNDRangeKernel(commands, kernel, 1,
NULL, &global, &local, 0, NULL, NULL);

## Slide 55
读取结果回来(这是一个阻塞操作（ blocking operation ）)。这里使用的是有序队列（in-order queue），就保证了在读取操作开始之前，前面的命令都已经执行完毕了。
err = clEnqueueReadBuffer(commands, d_c, CL_TRUE,
sizeof(float)*count, h_c, 0, NULL, NULL);
5. 命令排序（ Enqueue commands ）

## Slide 56
向量加法– 宿主程序
// 在一个 GPU 上面创建 OpenCL 上下文
cl_context context = clCreateContextFromType(0,
CL_DEVICE_TYPE_GPU, NULL, NULL, NULL);
// 获取连接到上下文的 GPU 设备列表
clGetContextInfo(context, CL_CONTEXT_DEVICES, 0, NULL, &cb);
cl_device_id[] devices = malloc(cb);
clGetContextInfo(context,CL_CONTEXT_DEVICES,cb,devices,NULL);
// 创建一个命令队列
cmd_queue = clCreateCommandQueue(context,devices[0],0,NULL);
// 分配缓存内存对象
memobjs[0] = clCreateBuffer(context, CL_MEM_READ_ONLY |
CL_MEM_COPY_HOST_PTR, sizeof(cl_float)*n, srcA, NULL);
memobjs[1] = clCreateBuffer(context, CL_MEM_READ_ONLY |
CL_MEM_COPY_HOST_PTR, sizeof(cl_float)*n, srcb, NULL);
memobjs[2] = clCreateBuffer(context, CL_MEM_WRITE_ONLY,
sizeof(cl_float)*n, NULL, NULL);
// 创建程序 program
program = clCreateProgramWithSource(context, 1,
&program_source, NULL, NULL);
// 构建程序 program
err = clBuildProgram(program, 0, NULL,NULL,NULL,NULL);
// 创建核函数 kernel
kernel = clCreateKernel(program, “vec_add”, NULL);
// 设定参数值 args values
err = clSetKernelArg(kernel, 0, (void *) &memobjs[0],
sizeof(cl_mem));
err |= clSetKernelArg(kernel, 1, (void *) &memobjs[1],
sizeof(cl_mem));
err |= clSetKernelArg(kernel, 2, (void *) &memobjs[2],
sizeof(cl_mem));
// 设定工作项维度 work-item dimensions
global_work_size[0] = n;
// 执行核函数 execute kernel
err = clEnqueueNDRangeKernel(cmd_queue, kernel, 1, NULL,
global_work_size, NULL,0,NULL,NULL);
// 读取输出数组 read output array
err = clEnqueueReadBuffer(cmd_queue, memobjs[2],
CL_TRUE, 0,
n*sizeof(cl_float), dst,
0, NULL, NULL);

## Slide 57
向量加法– 宿主程序
// 在一个 GPU 上面创建 OpenCL 上下文
cl_context context = clCreateContextFromType(0,
CL_DEVICE_TYPE_GPU, NULL, NULL, NULL);
// 获取连接到上下文的 GPU 设备列表
clGetContextInfo(context, CL_CONTEXT_DEVICES, 0, NULL, &cb);
cl_device_id[] devices = malloc(cb);
clGetContextInfo(context,CL_CONTEXT_DEVICES,cb,devices,NULL);
// 创建一个命令队列
cmd_queue = clCreateCommandQueue(context,devices[0],0,NULL);
// 分配缓存内存对象
memobjs[0] = clCreateBuffer(context, CL_MEM_READ_ONLY |
CL_MEM_COPY_HOST_PTR, sizeof(cl_float)*n, srcA, NULL);
memobjs[1] = clCreateBuffer(context, CL_MEM_READ_ONLY |
CL_MEM_COPY_HOST_PTR, sizeof(cl_float)*n, srcb, NULL);
memobjs[2] = clCreateBuffer(context, CL_MEM_WRITE_ONLY,
sizeof(cl_float)*n, NULL, NULL);
// 创建程序 program
program = clCreateProgramWithSource(context, 1,
&program_source, NULL, NULL);
// 构建程序 program
err = clBuildProgram(program, 0, NULL,NULL,NULL,NULL);
// 创建核函数 kernel
kernel = clCreateKernel(program, “vec_add”, NULL);
// 设定参数值 args values
err = clSetKernelArg(kernel, 0, (void *) &memobjs[0],
sizeof(cl_mem));
err |= clSetKernelArg(kernel, 1, (void *) &memobjs[1],
sizeof(cl_mem));
err |= clSetKernelArg(kernel, 2, (void *) &memobjs[2],
sizeof(cl_mem));
// 设定工作项维度 work-item dimensions
global_work_size[0] = n;
// 执行核函数 execute kernel
err = clEnqueueNDRangeKernel(cmd_queue, kernel, 1, NULL,
global_work_size, NULL,0,NULL,NULL);
// 读取输出数组 read output array
err = clEnqueueReadBuffer(cmd_queue, memobjs[2],
CL_TRUE, 0,
n*sizeof(cl_float), dst,
0, NULL, NULL);
定义平台 platform 和 命令队列queues
定义内存对象 memory objects
创建程序 program
构建程序 program
创建并设置核函数 kernel
执行核函数 kernel
读取结果到宿主 host
看上去可能挺复杂，但大部分其实都是样板套路，并没有那么麻烦。

## Slide 58
练习 2: 运行向量加法 Vadd 核函数
目标:
  尝试一下确保你能够运行一个 OpenCL 核函数。
流程:
  使用将以所提供的 C 语言的向量加法 Vadd 程序。可以运行为一个简单的核函数来实现两个向量相加。
  仔细阅读宿主代码，从中识别调用的 API。对比参考卡和这里的 API 描述。
  有一些辅助文件可以计算执行时间，输出设备简要信息，还可以用来查错。
预期输出:
  一条信息，证明向量加法成功运行。

## Slide 59
概览 OpenCL 接口（API）
章节 4

## Slide 60
宿主程序（Host program）可能很“丑陋（ugly）”
OpenCL 的目标是极致的可移植性，所以所有内容都是暴露在外的。
  (也就是说很啰嗦很详细)。
好在大多数情况下从一个程序到另一个程序，宿主代码（host code）都是一样的，这种复用（re-use）就使得这种啰嗦不算太大问题了。
你可以将常用的接口（API）打包成函数，甚至成为 C++或者 Python 里面的类，这样就可以更方便地复用这些类了。

## Slide 61
C++ 接口（Interface）
Khronos 公司定义了一个通用的 C++ 头文件，其中包含了 OpenCL 的高级接口，这个文件就是 cl.hpp
这个接口非常好用，对于 C++ 开发者来说特别简单。
主要特征:
  对平台（platform）和命令队列（command-queue）使用常用默认设置，节省了开发者的时间，避免去对最常见的部分内容重复编码。
  简化了基本接口（API），将关键参数（parameter）和对象（object）绑定，不在要求各种啰嗦又重复的参数列表。
  可以像一个常规函数一样，从宿主（host）来“调用（call）”一个核函数（kernel）。
  可以使用 C++ 的异常捕获机制来进行错误检查。

## Slide 62
C++ 接口: 设置宿主程序（host program）
启用 OpenCL 接口（API）的 异常捕获（Exceptions）。这一步需要在包含（include）头文件 cl.hpp 之前就先做好。
#define __CL_ENABLE_EXCEPTIONS
包含（include）关键头文件… 标准头文件和定制的都加入：
#include <CL/cl.hpp> // Khronos C++ 封装接口 API
#include <cstdio> // For C 风格
#include <iostream> // For C++ 风格输入输出
#include <vector> // For C++ 向量类型
想了解更多关于 C++ 的信息，可以参考后面的附录：
“针对 C 语言开发者的 C++ 指南”。

## Slide 63
// 创建缓存 buffers
// True 表示内存只读 CL_MEM_READ_ONLY
// False 表示内存可写 CL_MEM_READ_WRITE
d_a = cl::Buffer(context, h_a.begin(), h_a.end(), true);
d_b = cl::Buffer(context, h_b.begin(), h_b.end(), true);
d_c = cl::Buffer(context, CL_MEM_READ_WRITE, sizeof(float) * LENGTH);
// Enqueue the kernel
vadd(cl::EnqueueArgs(
queue,
cl::NDRange(count)),
d_a, d_b, d_c, count);
cl::copy(queue, d_c, h_c.begin(), h_c.end());
std::vector<float>
h_a(N), h_b(N), h_c(N);
// 初始化宿主向量…
cl::Buffer d_a, d_b, d_c;
cl::Context context( CL_DEVICE_TYPE_DEFAULT);
cl::CommandQueue queue(context);
cl::Program program(
context,
loadprogram(“vadd.cl”),
true);
// Create the kernel functor
cl::make_kernel<cl::Buffer, cl::Buffer, cl::Buffer, int>
vadd(program, “vadd”);
C++ 接口:
向量加法函数 Vadd 宿主程序（host program）

## Slide 64
C++ 缓存构造函数（Buffer Constructor）
下面是 API 中的定义:
  Buffer(startIterator, endIterator, bool readOnly, bool useHostPtr)
上面参数中的 readOnly 是一个布尔值（boolean），用于指定内存是只读状态 CL_MEM_READ_ONLY (true) 还是可写状态 CL_MEM_READ_WRITE (false)
  要注意，一定要指定好是真还是假。
上面参数中的 useHostPtr 也是一个布尔值（boolean）， 默认为假。
  因此迭代器（iterators）定义的数组（array）就暗含着被复制到（ implicitly copied ）设备内存（device memory）上了。
  如果你改设为 真（true）:
    迭代器所指定的内存就必须是连续的（contiguous）。
    上下文（context） 使用指针（uses the pointer）来指向宿主内存（host memory），这样宿主内存就成了设备可见（device accessible）的了，这和 CL_MEM_USE_HOST_PTR 一样。
    这个数组（array）并没有 复制到设备内存（device memory）。
在这个接口调用的时候，也可以制定一个上下文作为第一个参数（argument）。

## Slide 65
使用带有 C++ 向量迭代器的缓存构造函数的时候，要记得：
  这是一个阻塞调用（blocking call）；
  构造函数会讲一份副本队列传递给上下文（context）中的第一个设备（device）（当 useHostPtr == false 的时候）；
  如果你讲核函数队列到同一个上下文（context）下的另外的设备上，OpenCL 的运行环境（runtime）会 自动 确保缓存对象稍后被复制到对应设备上去。
C++ 缓存构造函数（Buffer Constructor）

## Slide 66
Python 接口
伊利诺伊大学香槟分校（ University of Illinois at Urbana-Champaign ）的 Andreas Klockner 开发了一个 Python 链接库
这个接口对于用户来说超级简单，而且不仅限于 Python 用户。
主要特征:
  辅助函数（helper functions）可以帮助用户在运行时（runtime）选择具体平台（platform）或者设备（device）
  getInfo() 方法成了类的属性，就不需要再去调用方法本身了。
  将一个核函数（kernel）当作一个方法进行调用。
  支持多行字符串，再也不需要另起很多行了。

## Slide 67
Python 接口： 设置宿主程序（host program）
导入 pyopencl 这个库
import pyopencl as cl
导入 numpy 以使用各种数组 arrays 等等.
import numpy
有的例子中使用辅助函数来输出一些有用信息
import deviceinfo

## Slide 68
N = 1024
# 创建上下文，命令队列，程序 create context, queue and program
context = cl.create_some_context()
queue = cl.CommandQueue(context)
kernelsource = open(‘vadd.cl’).read()
program = cl.Program(context, kernelsource).build()
# 创建宿主数组 create host arrays
h_a = numpy.random.rand(N).astype(float32)
h_b = numpy.random.rand(N).astype(float32)
h_c = numpy.empty(N).astype(float32)
# 创建设备缓存 create device buffers
mf = cl.mem_flags
d_a = cl.Buffer(context, mf.READ_ONLY | mf.COPY_HOST_PTR, hostbuf=h_a)
d_b = cl.Buffer(context, mf.READ_ONLY | mf.COPY_HOST_PTR, hostbuf=h_b)
d_c = cl.Buffer(context, mf.WRITE_ONLY, h_c.nbytes)
# 运行核函数 run kernel
vadd = program.vadd
vadd.set_scalar_arg_dtypes([None, None, None, numpy.uint32])
vadd(queue, h_a.shape, None, d_a, d_b, d_c, N)
# 返回结果 return results
cl.enqueue_copy(queue, h_c, d_c)

## Slide 69
练习3: 运行向量加法核函数Vadd kernel (C++ / Python)
目标：
  学习使用 OpenCL 接口（API）的 C++ 或者 Python 接口。
流程：
  测试讲义中提供的程序代码。这份代码会简单将两个向量求和。
  阅读宿主代码（host code），从中识别接口调用（API calls）。注意一下从 OpenCL 接口调用（API call）搭配 C++ 或者 Python 构建之间的对应关系。
  将原生的 C 语言代码和 C++ 或者 Python 版本代码进行对比。
  感受一下通用接口调用（common API calls）的简洁（simplicity）。
预期输出:
  一条信息，验证向量相加运算成功完成。

## Slide 70
练习 4: 链接向量加法核函数 Vadd kernels (C++ / Python)
目标：
  检验你是否理解了如何操纵核函数调用（kernel invocations）以及 OpenCL 里面的缓存（buffer）。
流程：
  在 C++ 或者 Python 中启动一个向量加法程序 VADD program ；
  增加额外的缓存对象（buffer objects）然后赋值成定义在宿主（host）上的向量（可以参考文中提供的 vadd 这个向量加法函数然后进行修改）；
  将多个向量加法链接起来 … 比如 C=A+B; D=C+E; F=D+G；
  读取最终结果，验证一下是否正确；
  对比 C语言 和宿主代码（host code）程序的复杂程度。
预期输出:
  一条信息，标准化输出，证明向量的链式相加得到了正确结果。
(简单的解决方案就是对于 C = A + B; D = C + E; F = D + G; 返回 F)

## Slide 71
宿主角度（hosts view）理解核函数（kernels）
复习
Notes: 71

## Slide 72
处理核函数（Kernels）(C++)
在 OpenCL 程序中，所有动作都发生在核函数内。
使用核函数的步骤如下：
  从文件中加载核函数源代码到一个程序对象（program object）中。
  在这个程序内从一个函数创建一个核仿函数（kernel functor）。
  初始化设备内存（device memory）。
  调用核仿函数（ kernel functor ），指定内存对象（memory objects）以及全局、局域规模（ global/local sizes ）。
  从设备读取结果。
要注意核函数的参数列表一定要和宿主（host）上的核函数定义相符合。

## Slide 73
创建一个核函数（kernel）
核代码可以是宿主代码（host code）中的一个字符串 (样例代码)
或者也可以从一个文件中进行加载 (真实案例)
在默认上下文（context）环境下为默认设备（devices）编译
program.build();
在程序内从一个函数定义核仿函数（kernel functor） – 这样就可以“调用”核函数去进行队列（enqueue）：
cl::make_kernel
<cl::Buffer, cl::Buffer, cl::Buffer, int> vadd(program, "vadd");
构建这一步可以在程序构造函数（program constructor）中设置为 true 来实现。如果你需要设置具体的构建标志（flag），那就要在构造函数（constructor）中设置为 false，然后在用的时候再调用这个方法（method）。

## Slide 74
如果你要查询一个核函数的信息，你也需要创建一个核对象：
cl::Kernel ko_vadd(program, “vadd”);
获取局部维度的默认规模（比如，工作组的规模）
::size_t local = ko_vadd.getWorkGroupInfo
<CL_KERNEL_WORK_GROUP_SIZE>(cl::Device::getDefault());
如果我们自己设置了局部维度（local dimension）或者接受了 OpenCL 的默认设置，就不需要这一步。
可以使用在 OpenCL 1.1 版本中的表格5.15所包含的任意工作组信息。
这个函数会返回适当的类型。
创建一个核函数（进阶版）

## Slide 75
附加参数（args）以及队列核函数（enqueue kernel）
将核函数提交队列以执行，缓存对象（ buffer objects ）包括 d_a, d_b 和 d_c 以及其长度（length）,和个数计数（count）:
vadd(cl::EnqueueArgs(
queue, cl::NDRange(count), cl::NDRange(local)), d_a, d_b, d_c, count);
这里可以包含来自 clEnqueueNDRangeKernel 函数的任意参数，包括事件等待列表（Event wait lists，这个后面再讲）以及命令队列（command queue，可选）。

## Slide 76
处理核函数（Kernels）(Python)
核函数的代码字符串可以使用三个英文单引号来进行定义，不需要另起一行：
source = ‘‘‘
__kernel void func() {}
’’’
或者可以在一个文件中，在运行的时候加载上来：
source = open(‘file.cl’).read()
然后程序对象（program object）就可以创建和构建了：
prg = pyopencl.Program(context,source).build()

## Slide 77
核函数可以被当做已构建的程序对象（built program object）的一个方法（method）来调用，如下
program.kernel(q, t, l, a)
上面的调用中的基本参数（basic arguments）包括：
  q 是命令队列（command queue）
  t 是全局规模（global size），定义成了元组，比如： (x, ), (x,y), or (x,y,z)
  l 是一个元组的局部规模（local size）或者 None
  a 是传递到核函数的参数列表
    标量（scalar）必须转成 numpy 的类型，比如 numpy.uint32(var), numpy.float32(var) 等
处理核函数（Kernels）(Python)

## Slide 78
在程序对象（program object）中调用核函数就会调用 C API 中的 clCreateKernel()
  也就是调用 program.kernel() 每次创建核对象（kernel object），这是不必须的（unnecessary）。
拉出核函数就可以停止（pull out the kernel to stop）:
kernel = program.kernel
在核对象上指定标量参数来保存在核函数执行调用中的类型转换：
kernel.set_scalar_arg_dtypes([list, of, arg, types])
  缓存（buffer）和局部内存（local memory）参数都应该被设为 None
  标量参数（scalar arguments）需要被转成 numpy 格式，比如 numpy.float32, numpy.uint32, 等等。
处理核函数（Kernels）(Python)

## Slide 79
练习 5: The D = A + B + C problem
目标:
  验证你理解了如何控制核函数（kernel）中的参数定义（argument definition）
  验证你理解了宿主（host）/核（kernel）的接口（interface）
流程：
  启动一个向量加法程序 VADD
  修改核代码（kernel code）使之能够将三个向量进行相加
  修改宿主代码（host code）使之定义三个向量，然后作为对应的核函数参数赋值给核函数
  读取回来最终结果，验证是否正确
预期输出:
  检测输出结果看看是否正确。将验证消息打印到显示器上。

## Slide 80
至此已经讲到了 OpenCL 中的基本平台（basic platform）和运行时环境接口（runtime API)的基本信息
arg [0] value
arg [1] value
arg [2] value
arg [0] value
arg [1] value
arg [2] value
In Order
Queue
Out of Order
Queue
GPU
上下文 Context
__kernel void
dp_mul(global const float *a,
global const float *b,
global float *c)
{
int id = get_global_id(0);
c[id] = a[id] * b[id]; }
dp_mul
CPU 程序二进制文件
dp_mul
GPU 程序二进制文件
Programs
arg[0] value
arg[1] value
arg[2] value
缓存
Buffers
图像
Images
有序队列
In Order
Queue
无序队列
Out of Order
Queue
计算设备Compute Device
GPU
CPU
dp_mul
程序
Programs
核函数
Kernels
内存对象
Memory Objects
命令队列
Command Queues
编译代码
Compile code
创建数据和参数
Create data & arguments
发送执行
Send to execution

## Slide 81
Introduction to OpenCL kernel programming
章节 5
Notes: 81

## Slide 82
OpenCL C for Compute Kernels
Derived from ISO C99
  A few restrictions: no recursion, function pointers, functions in C99 standard headers ...
  Preprocessing directives defined by C99 are supported (#include etc.)
Built-in data types
  Scalar and vector data types, pointers
  Data-type conversion functions:
    convert_type<_sat><_roundingmode>
  Image types:
    image2d_t, image3d_t and sampler_t

## Slide 83
OpenCL C for Compute Kernels
Built-in functions — mandatory
  Work-Item functions, math.h, read and write image
  Relational, geometric functions, synchronization functions
  printf (v1.2 only, so not currently for NVIDIA GPUs)
Built-in functions — optional (called “extensions”)
  Double precision, atomics to global and local memory
  Selection of rounding mode, writes to image3d_t surface

## Slide 84
OpenCL C Language Highlights
Function qualifiers
  __kernel qualifier declares a function as a kernel
    I.e. makes it visible to host code so it can be enqueued
  Kernels can call other kernel-side functions
Address space qualifiers
  __global, __local, __constant, __private
  Pointer kernel arguments must be declared with an address space qualifier
Work-item functions
  get_work_dim(), get_global_id(), get_local_id(), get_group_id()
Synchronization functions
  Barriers - all work-items within a work-group must execute the barrier function before any work-item can continue
  Memory fences - provides ordering between memory operations

## Slide 85
OpenCL C Language Restrictions
Pointers to functions are not allowed
Pointers to pointers allowed within a kernel, but not as an argument to a kernel invocation
Bit-fields are not supported
Variable length arrays and structures are not supported
Recursion is not supported (yet!)
Double types are optional in OpenCL v1.1, but the key word is reserved
(note: most implementations support double)

## Slide 86
1 | 2 | 1 | x |  | 1
1 | 3 | 3 | y | = | 2
1 | 1 | 4 | z |  | 6
Worked example: Linear Algebra
Definition:
  The branch of mathematics concerned with the study of vectors, vector spaces, linear transformations and systems of linear equations.
Example: Consider the following system of linear equations
x + 2y + z = 1
x + 3y + 3z = 2
x + y + 4z = 6
  This system can be represented in terms of vectors and a matrix as the classic “Ax = b” problem.

## Slide 87
1 | 0 | 0 |  | 1 | 2 | 1 |  | 1 | 2 | 1
1 | 1 | 0 |  | 0 | 1 | 2 | = | 1 | 3 | 3
1 | -1 | 1 |  | 0 | 0 | 5 |  | 1 | 2 | 4
Solving Ax=b
LU Decomposition:
  transform a matrix into the product of a lower triangular and upper triangular matrix. It is used to solve a linear system of equations.
L
A
U
=
We solve for x, given a problem Ax=b
  Ax=b LUx=b
  Ux=(L-1)b x = (U-1)(L-1)b
So we need to be able to do matrix multiplication

## Slide 88
void mat_mul(int N, float *A, float *B, float *C)
{
int i, j, k;
for (i = 0; i < N; i++) {
for (j = 0; j < N; j++) {
C[i*N+j] = 0.0f;
for (k = 0; k < N; k++) {
// C(i, j) = sum(over k) A(i,k) * B(k,j)
C[i*N+j] += A[i*N+k] * B[k*N+j];
}
}
}
}
Matrix multiplication: sequential code
We calculate C=AB, where all three matrices are NxN
=
x
A(i,:)
B(:,j)
C(i,j)
Dot product of a row of A and a column of B for each element of C

## Slide 89
Matrix multiplication performance
Serial C code on CPU (single core).
Case | MFLOPS | 
 | CPU | GPU
Sequential C (not OpenCL) | 887.2 | N/A
Device is Intel® Xeon® CPU, E5649 @ 2.53GHz using the gcc compiler.
第三方名称是其公司所有财产
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.

## Slide 90
Matrix multiplication: sequential code
void mat_mul(int N, float *A, float *B, float *C)
{
int i, j, k;
for (i = 0; i < N; i++) {
for (j = 0; j < N; j++) {
C[i*N+j] = 0.0f;
for (k = 0; k < N; k++) {
// C(i, j) = sum(over k) A(i,k) * B(k,j)
C[i*N+j] += A[i*N+k] * B[k*N+j];
}
}
}
}
We turn this into an OpenCL kernel!

## Slide 91
Matrix multiplication: OpenCL kernel (1/2)
void mat_mul(int N, float *A, float *B, float *C)
{
int i, j, k;
for (i = 0; i < N; i++) {
for (j = 0; j < N; j++) {
// C(i, j) = sum(over k) A(i,k) * B(k,j)
for (k = 0; k < N; k++) {
C[i*N+j] += A[i*N+k] * B[k*N+j];
}
}
}
}
__kernel void mat_mul(
const int N,
__global float *A, __global float *B, __global float *C)
Mark as a kernel function and specify memory qualifiers
Notes: 91

## Slide 92
__kernel void mat_mul(
const int N,
__global float *A, __global float *B, __global float *C)
{
int i, j, k;
for (i = 0; i < N; i++) {
for (j = 0; j < N; j++) {
for (k = 0; k < N; k++) {
// C(i, j) = sum(over k) A(i,k) * B(k,j)
C[i*N+j] += A[i*N+k] * B[k*N+j];
}
}
}
}
Matrix multiplication: OpenCL kernel (2/2)
i = get_global_id(0);
j = get_global_id(1);
Remove outer loops and set work-item co-ordinates
Notes: 92

## Slide 93
__kernel void mat_mul(
const int N,
__global float *A, __global float *B, __global float *C)
{
int i, j, k;
i = get_global_id(0);
j = get_global_id(1);
// C(i, j) = sum(over k) A(i,k) * B(k,j)
for (k = 0; k < N; k++) {
C[i*N+j] += A[i*N+k] * B[k*N+j];
}
}
Matrix multiplication: OpenCL kernel
Notes: 93

## Slide 94
__kernel void mmul(
const int N,
__global float *A,
__global float *B,
__global float *C)
Matrix multiplication: OpenCL kernel improved
{
int k;
int i = get_global_id(0);
int j = get_global_id(1);
float tmp = 0.0f;
for (k = 0; k < N; k++)
tmp += A[i*N+k]*B[k*N+j];
}
C[i*N+j] += tmp;
}
Rearrange and use a local scalar for intermediate C element values (a common optimization in Matrix Multiplication functions)
Notes: 94

## Slide 95
Matrix multiplication host program (C++ API)
int main(int argc, char *argv[])
{
std::vector<float> h_A, h_B, h_C; // matrices
int Mdim, Ndim, Pdim; // A[N][P],B[P][M],C[N][M]
int i, err;
int szA, szB, szC; // num elements in each matrix
double start_time, run_time; // timing data
cl::Program program;
Ndim = Pdim = Mdim = ORDER;
szA = Ndim*Pdim;
szB = Pdim*Mdim;
szC = Ndim*Mdim;
h_A = std::vector<float>(szA);
h_B = std::vector<float>(szB);
h_C = std::vector<float>(szC);
initmat(Mdim, Ndim, Pdim, h_A, h_B, h_C);
// Compile for first kernel to setup program
program = cl::Program(C_elem_KernelSource, true);
Context context(CL_DEVICE_TYPE_DEFAULT);
cl::CommandQueue queue(context);
std::vector<Device> devices =
context.getInfo<CL_CONTEXT_DEVICES>();
cl::Device device = devices[0];
std::string s =
device.getInfo<CL_DEVICE_NAME>();
std::cout << "\nUsing OpenCL Device ”
<< s << "\n";
// Setup the buffers, initialize matrices,
// and write them into global memory
initmat(Mdim, Ndim, Pdim, h_A, h_B, h_C);
cl::Buffer d_a(context, h_A.begin(),h_A.end(), true);
cl::Buffer d_b(context, h_B.begin(),h_B.end(), true);
cl::Buffer d_c = cl::Buffer(context,
CL_MEM_WRITE_ONLY,
sizeof(float) * szC);
cl::make_kernel<int, int, int,
cl::Buffer, cl::Buffer, cl::Buffer>
naive(program, "mmul");
zero_mat(Ndim, Mdim, h_C);
start_time = wtime();
naive(cl::EnqueueArgs(queue,
cl::NDRange(Ndim, Mdim)),
Ndim, Mdim, Pdim, d_a, d_b, d_c);
cl::copy(queue, d_c, h_C.begin(), h_C.end());
run_time = wtime() - start_time;
results(Mdim, Ndim, Pdim, h_C, run_time);
}
Declare and initialize data
Setup the platform and build program
Setup buffers and write A and B matrices to the device memory
Create the kernel functor
Run the kernel and collect results
Note: To use the default context/queue/device, skip this section and remove the references to context, queue and device.

## Slide 96
Matrix multiplication performance
Matrices are stored in global memory.
Case | MFLOPS | 
 | CPU | GPU
Sequential C (not OpenCL) | 887.2 | N/A
C(i,j) per work-item, all global | 3,926.1 | 3,720.9
Device is Tesla® M2090 GPU from NVIDIA® with a max of 16 compute units, 512 PEs
Device is Intel® Xeon® CPU, E5649 @ 2.53GHz
第三方名称是其公司所有财产
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.

## Slide 97
练习 6: Matrix Multiplication
目标：
  To write your first complete OpenCL kernel “from scratch”
  To multiply a pair of matrices
流程：
  Start with the provided matrix multiplication OpenCL host program including the function to generate matrices and test results
  Create a kernel to do the multiplication
  Modify the provided OpenCL host program to use your kernel
  Verify the results
预期输出:
  A message to standard output verifying that the chain of vector additions produced the correct result
  Report the runtime and the MFLOPS

## Slide 98
Understanding the OpenCL memory hierarchy
章节 6

## Slide 99
Optimizing matrix multiplication
MM cost determined by FLOPS and memory movement:
  2*n3 = O(n3) FLOPS
  Operates on 3*n2 = O(n2) numbers
To optimize matrix multiplication, we must ensure that for every memory access we execute as many FLOPS as possible.
Outer product algorithms are faster, but for pedagogical reasons, let’s stick to the simple dot-product algorithm.
We will work with work-item/work-group sizes and the memory model to optimize matrix multiplication
=
x
A(i,:)
B(:,j)
C(i,j)
Dot product of a row of A and a column of B for each element of C

## Slide 100
An N-dimensional domain of work-items
Global Dimensions:
  1024x1024 (whole problem space)
Local Dimensions:
  128x128 (work-group, executes together)
Choose the dimensions that are “best” for your algorithm
1024
1024
Synchronization between work-items possible only within work-groups:
barriers and memory fences
Cannot synchronize between work-groups within a kernel

## Slide 101
OpenCL Memory model
Private Memory
  Per work-item
Local Memory
  Shared within a
work-group
Global/Constant Memory
  Visible to all
work-groups
Host memory
  On the CPU
Memory management is explicit: You are responsible for moving data from
host → global → local and back

## Slide 102
OpenCL Memory model
Private Memory
  Fastest & smallest: O(10) words/WI
Local Memory
  Shared by all WI’s in a work-group
  But not shared between work-groups!
  O(1-10) Kbytes per work-group
Global/Constant Memory
  O(1-10) Gbytes of Global memory
  O(10-100) Kbytes of Constant memory
Host memory
  On the CPU - GBytes
Memory management is explicit: O(1-10) Gbytes/s bandwidth to discrete GPUs for
Host <-> Global transfers

## Slide 103
Private Memory
Managing the memory hierarchy is one of the most important things to get right to achieve good performance
Private Memory:
  A very scarce resource, only a few tens of 32-bit words per Work-Item at most
  If you use too much it spills to global memory or reduces the number of Work-Items that can be run at the same time, potentially harming performance*
  Think of these like registers on the CPU
* Occupancy on a GPU

## Slide 104
Local Memory*
Tens of KBytes per Compute Unit
  As multiple Work-Groups will be running on each CU, this means only a fraction of the total Local Memory size is available to each Work-Group
Assume O(1-10) KBytes of Local Memory per Work-Group
  Your kernels are responsible for transferring data between Local and Global/Constant memories … there are optimized library functions to help
  E.g. async_work_group_copy(), async_workgroup_strided_copy(), …
Use Local Memory to hold data that can be reused by all the work-items in a work-group
Access patterns to Local Memory affect performance in a similar way to accessing Global Memory
  Have to think about things like coalescence & bank conflicts
* Typical figures for a 2013 GPU

## Slide 105
Local Memory
Local Memory doesn’t always help…
  CPUs don’t have special hardware for it
  This can mean excessive use of Local Memory might slow down kernels on CPUs
  GPUs now have effective on-chip caches which can provide much of the benefit of Local Memory but without programmer intervention
  So, your mileage may vary!

## Slide 106
The Memory Hierarchy
Private memory
O(10) words/WI
Local memory
O(1-10) KBytes/WG
Global memory
O(1-10) GBytes
Host memory
O(1-100) GBytes
Private memory
O(2-3) words/cycle/WI
Local memory
O(10) words/cycle/WG
Global memory
O(100-200) GBytes/s
Host memory
O(1-100) GBytes/s
Speeds and feeds approx. for a high-end discrete GPU, circa 2011
Bandwidths
Sizes

## Slide 107
Memory Consistency
OpenCL uses a relaxed consistency memory model; i.e.
  The state of memory visible to a work-item is not guaranteed to be consistent across the collection of work-items at all times.
Within a work-item:
  Memory has load/store consistency to the work-item’s private view of memory, i.e. it sees its own reads and writes correctly
Within a work-group:
  Local memory is consistent between work-items at a barrier.
Global memory is consistent within a work-group at a barrier, but not guaranteed across different work-groups!!
  This is a common source of bugs!
Consistency of memory shared between commands (e.g. kernel invocations) is enforced by synchronization (barriers, events, in-order queue)

## Slide 108
Optimizing matrix multiplication
There may be significant overhead to manage work-items and work-groups.
So let’s have each work-item compute a full row of C
=
x
A(i,:)
B(:,j)
C(i,j)
Dot product of a row of A and a column of B for each element of C
And with an eye towards future optimizations, let’s collect work-items into work-groups with 64 work-items per work-group

## Slide 109
An N-dimension domain of work-items
Global Dimensions: 1024 (1D)
Whole problem space (index space)
Local Dimensions: 64 (work-items per work-group)
Only 1024/64 = 16 work-groups in total
Important implication: we will have a lot fewer work-items per work-group (64) and work-groups (16). Why might this matter?
1024
64

## Slide 110
__kernel void mmul(
const int N,
__global float *A,
__global float *B,
__global float *C)
Matrix multiplication: One work item per row of C
{
int j, k;
int i = get_global_id(0);
float tmp;
for (j = 0; j < N; j++) {
tmp = 0.0f;
for (k = 0; k < N; k++)
tmp += A[i*N+k]*B[k*N+j];
C[i*N+j] = tmp;
}
}
Notes: 110

## Slide 111
// Setup the buffers, initialize matrices,
// and write them into global memory
initmat(Mdim, Ndim, Pdim, h_A, h_B, h_C);
cl::Buffer d_a(context, h_A.begin(),h_A.end(), true);
cl::Buffer d_b(context, h_B.begin(),h_B.end(), true);
cl::Buffer d_c = cl::Buffer(context,
CL_MEM_WRITE_ONLY,
sizeof(float) * szC);
cl::make_kernel<int, int, int,
cl::Buffer, cl::Buffer, cl::Buffer>
krow(program, "mmul");
zero_mat(Ndim, Mdim, h_C);
start_time = wtime();
krow(cl::EnqueueArgs(queue,
cl::NDRange(Ndim),
cl::NDRange(ORDER/16)),
Ndim, Mdim, Pdim, d_a, d_b, d_c);
cl::copy(queue, d_c, h_C.begin(), h_C.end());
run_time = wtime() - start_time;
results(Mdim, Ndim, Pdim, h_C, run_time);
}
int main(int argc, char *argv[])
{
std::vector<float> h_A, h_B, h_C; // matrices
int Mdim, Ndim, Pdim; // A[N][P],B[P][M],C[N][M]
int i, err;
int szA, szB, szC; // num elements in each matrix
double start_time, run_time; // timing data
cl::Program program;
Ndim = Pdim = Mdim = ORDER;
szA = Ndim*Pdim;
szB = Pdim*Mdim;
szC = Ndim*Mdim;
h_A = std::vector<float>(szA);
h_B = std::vector<float>(szB);
h_C = std::vector<float>(szC);
initmat(Mdim, Ndim, Pdim, h_A, h_B, h_C);
// Compile for first kernel to setup program
program = cl::Program(C_elem_KernelSource, true);
Context context(CL_DEVICE_TYPE_DEFAULT);
cl::CommandQueue queue(context);
std::vector<Device> devices =
context.getInfo<CL_CONTEXT_DEVICES>();
cl::Device device = devices[0];
std::string s =
device.getInfo<CL_DEVICE_NAME>();
std::cout << "\nUsing OpenCL Device ”
<< s << "\n";
Matrix multiplication host program (C++ API)
Changes to host program:
  1D ND Range set to number of rows in the C matrix
  Local Dimension set to 64 so number of work-groups match number of compute units (16 in this case) for our order 1024 matrices
krow(cl::EnqueueArgs(queue
cl::NDRange(Ndim),
cl::NDRange(ORDER/16)),
Ndim, Mdim, Pdim, a_in, b_in, c_out);

## Slide 112
Matrix multiplication performance
Matrices are stored in global memory.
Case | MFLOPS | 
 | CPU | GPU
Sequential C (not OpenCL) | 887.2 | N/A
C(i,j) per work-item, all global | 3,926.1 | 3,720.9
C row per work-item, all global | 3,379.5 | 4,195.8
Device is Tesla® M2090 GPU from NVIDIA® with a max of 16 compute units, 512 PEs
Device is Intel® Xeon® CPU, E5649 @ 2.53GHz
第三方名称是其公司所有财产
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.
This has started to help.

## Slide 113
Optimizing matrix multiplication
Notice that, in one row of C, each element reuses the same row of A.
Let’s copy that row of A into private memory of the work-item that’s (exclusively) using it to avoid the overhead of loading it from global memory for each C(i,j) computation.
=
x
A(i,:)
B(:,j)
C(i,j)
Private memory of each work-item

## Slide 114
__kernel void mmul(
const int N,
__global float *A,
__global float *B,
__global float *C)
{
int j, k;
int i = get_global_id(0);
float tmp;
float Awrk[1024];
Matrix multiplication: (Row of A in private memory)
for (k = 0; k < N; k++)
Awrk[k] = A[i*N+k];
for (j = 0; j < N; j++) {
tmp = 0.0f;
for (k = 0; k < N; k++)
tmp += Awrk[k]*B[k*N+j];
C[i*N+j] += tmp;
}
}
(*Actually, this is using far more private memory than we’ll have and so Awrk[] will be spilled to global memory)
Copy a row of A into private memory from global memory before we start with the matrix multiplications.
Setup a work array for A in private memory*
Notes: 114

## Slide 115
Matrix multiplication performance
Matrices are stored in global memory.
Case | MFLOPS | 
 | CPU | GPU
Sequential C (not OpenCL) | 887.2 | N/A
C(i,j) per work-item, all global | 3,926.1 | 3,720.9
C row per work-item, all global | 3,379.5 | 4,195.8
C row per work-item, A row private | 3,385.8 | 8,584.3
Device is Tesla® M2090 GPU from NVIDIA® with a max of 16 compute units, 512 PEs
Device is Intel® Xeon® CPU, E5649 @ 2.53GHz
第三方名称是其公司所有财产
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.
Big impact!

## Slide 116
Why using too much private memory can be a good thing
In reality private memory is just hardware registers, so only dozens of these are available per work-item
Many kernels will allocate too many variables to private memory
So the compiler already has to be able to deal with this
It does so by spilling excess private variables to (global) memory
You still told the compiler something useful – that the data will only be accessed by a single work-item
This lets the compiler allocate the data in such as way as to enable more efficient memory access
Notes: 116

## Slide 117
练习 7: using private memory
目标：
  Use private memory to minimize memory movement costs and optimize performance of your matrix multiplication program
流程：
  Start with your matrix multiplication solution
  Modify the kernel so that each work-item copies its own row of A into private memory
  Optimize step by step, saving the intermediate versions and tracking performance improvements
预期输出:
  A message to standard output verifying that the matrix multiplication program is generating the correct results
  Report the runtime and the MFLOPS

## Slide 118
Optimizing matrix multiplication
We already noticed that, in one row of C, each element uses the same row of A
Each work-item in a work-group also uses the same columns of B
So let’s store the B columns in local memory (which is shared by the work-items in the work-group)
=
x
A(i,:)
B(:,j)
C(i,j)
Private memory of each work-item
Local memory for each work-group

## Slide 119
__kernel void mmul(
const int N,
__global float *A,
__global float *B,
__global float *C,
__local float *Bwrk)
{
int j, k;
int i = get_global_id(0);
int iloc = get_local_id(0);
int nloc = get_local_size(0);
float tmp;
float Awrk[1024];
Matrix multiplication: B column shared between work-items
for (k = 0; k < N; k++)
Awrk[k] = A[i*N+k];
for (j = 0; j < N; j++) {
for (k=iloc; k<N; k+=nloc)
Bwrk[k] = B[k* N+j];
barrier(CLK_LOCAL_MEM_FENCE);
tmp = 0.0f;
for (k = 0; k < N; k++)
tmp += Awrk[k]*Bwrk[k];
C[i*N+j] = tmp;
barrier(CLK_LOCAL_MEM_FENCE);
}
}
Pass a work array in local memory to hold a column of B. All the work-items do the copy “in parallel” using a cyclic loop distribution (hence why we need iloc and nloc)
Notes: 119

## Slide 120
// Setup the buffers, initialize matrices,
// and write them into global memory
initmat(Mdim, Ndim, Pdim, h_A, h_B, h_C);
cl::Buffer d_a(context, h_A.begin(),h_A.end(), true);
cl::Buffer d_b(context, h_B.begin(),h_B.end(), true);
cl::Buffer d_c = cl::Buffer(context,
CL_MEM_WRITE_ONLY,
sizeof(float) * szC);
cl::make_kernel<int, int, int,
cl::Buffer, cl::Buffer, cl::Buffer>
rowcol(program, "mmul");
zero_mat(Ndim, Mdim, h_C);
start_time = wtime();
rowcol(cl::EnqueueArgs(queue,
cl::NDRange(Ndim),
cl::NDRange(ORDER/16)),
Ndim, Mdim, Pdim, d_a, d_b, d_c);
cl::copy(queue, d_c, h_C.begin(), h_C.end());
run_time = wtime() - start_time;
results(Mdim, Ndim, Pdim, h_C, run_time);
}
int main(int argc, char *argv[])
{
std::vector<float> h_A, h_B, h_C; // matrices
int Mdim, Ndim, Pdim; // A[N][P],B[P][M],C[N][M]
int i, err;
int szA, szB, szC; // num elements in each matrix
double start_time, run_time; // timing data
cl::Program program;
Ndim = Pdim = Mdim = ORDER;
szA = Ndim*Pdim;
szB = Pdim*Mdim;
szC = Ndim*Mdim;
h_A = std::vector<float>(szA);
h_B = std::vector<float>(szB);
h_C = std::vector<float>(szC);
initmat(Mdim, Ndim, Pdim, h_A, h_B, h_C);
// Compile for first kernel to setup program
program = cl::Program(C_elem_KernelSource, true);
Context context(CL_DEVICE_TYPE_DEFAULT);
cl::CommandQueue queue(context);
std::vector<Device> devices =
context.getInfo<CL_CONTEXT_DEVICES>();
cl::Device device = devices[0];
std::string s =
device.getInfo<CL_DEVICE_NAME>();
std::cout << "\nUsing OpenCL Device ”
<< s << "\n";
Matrix multiplication host program (C++ API)
cl::LocalSpaceArg localmem =
cl::Local(sizeof(float) * Pdim);
rowcol(cl::EnqueueArgs(queue,
cl::NDRange(Ndim),
cl::NDRange(ORDER/16)),
Ndim, Mdim, Pdim, d_a, d_b, d_c, localmem);
Changes to host program:
  Pass local memory to kernels.
    This requires a change to the kernel argument lists … an arg of type LocalSpaceArg is needed.
    Allocate the size of local memory
    Update argument list in kernel functor
cl::make_kernel<int, int, int,
cl::Buffer, cl::Buffer, cl:::Buffer,
cl::LocalSpaceArg>
rowcol(program, “mmul”);

## Slide 121
Matrix multiplication performance
Matrices are stored in global memory.
Case | MFLOPS | 
 | CPU | GPU
Sequential C (not OpenCL) | 887.2 | N/A
C(i,j) per work-item, all global | 3,926.1 | 3,720.9
C row per work-item, all global | 3,379.5 | 4,195.8
C row per work-item, A row private | 3,385.8 | 8,584.3
C row per work-item, A private, B local | 10,047.5 | 8,181.9
Device is Tesla® M2090 GPU from NVIDIA® with a max of 16 compute units, 512 PEs
Device is Intel® Xeon® CPU, E5649 @ 2.53GHz
第三方名称是其公司所有财产
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.

## Slide 122
Making matrix multiplication really fast
Our 目标 has been to describe how to work with private, local and global memory. We’ve ignored many well-known techniques for making matrix multiplication fast
  The number of work items must be a multiple of the fundamental machine “vector width”. This is the wavefront on AMD, warp on NVIDIA, and the number of SIMD lanes exposed by vector units on a CPU
  To optimize reuse of data, you need to use blocking techniques
    Decompose matrices into tiles such that three tiles just fit in the fastest (private) memory
    Copy tiles into local memory
    Do the multiplication over the tiles
  We modified the matrix multiplication program provided with the NVIDIA OpenCL SDK to work with our test suite to produce the blocked results on the following slide. This used register blocking with block sizes mapped onto the GPU’s warp size

## Slide 123
Matrix multiplication performance
Matrices are stored in global memory.
Case | MFLOPS | 
 | CPU | GPU
Sequential C (not OpenCL) | 887.2 | N/A
C(i,j) per work-item, all global | 3,926.1 | 3,720.9
C row per work-item, all global | 3,379.5 | 4,195.8
C row per work-item, A row private | 3,385.8 | 8,584.3
C row per work-item, A private, B local | 10,047.5 | 8,181.9
Block oriented approach using local | 1,534.0 | 230,416.7
Device is Tesla® M2090 GPU from NVIDIA® with a max of 16 compute units, 512 PEs
Device is Intel® Xeon® CPU, E5649 @ 2.53GHz
第三方名称是其公司所有财产
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.
Biggest impact so far!

## Slide 124
练习 8: using local memory
目标：
  Use local memory to minimize memory movement costs and optimize performance of your matrix multiplication program
流程：
  Start with your matrix multiplication solution that already uses private memory from 练习 7
  Modify the kernel so that each work-group collaboratively copies its own column of B into local memory
  Optimize step by step, saving the intermediate versions and tracking performance improvements
预期输出:
  A message to standard output verifying that the matrix multiplication program is generating the correct results
  Report the runtime and the MFLOPS
Extra:
  Look at the fast, blocked implementation from the NVIDIA OpenCL SDK example. Try running it and compare to yours

## Slide 125
Synchronization in OpenCL
章节 7

## Slide 126
Consider N-dimensional domain of work-items
Global Dimensions:
  1024x1024 (whole problem space)
Local Dimensions:
  64x64 (work-group, executes together)
Synchronization: when multiple units of execution (e.g. work-items) are brought to a known point in their execution. Most common example is a barrier … i.e. all units of execution “in scope” arrive at the barrier before any proceed.
1024
1024
Synchronization between work-items possible only within work-groups:
barriers and memory fences
Cannot synchronize between work-groups within a kernel

## Slide 127
Work-Item Synchronization
Within a work-group
void barrier()
  Takes optional flags
CLK_LOCAL_MEM_FENCE and/or CLK_GLOBAL_MEM_FENCE
  A work-item that encounters a barrier() will wait until ALL work-items in its work-group reach the barrier()
  Corollary: If a barrier() is inside a branch, then the branch must be taken by either:
    ALL work-items in the work-group, OR
    NO work-item in the work-group
Across work-groups
  No guarantees as to where and when a particular work-group will be executed relative to another work-group
  Cannot exchange data, or have barrier-like synchronization between two different work-groups! (Critical issue!)
  Only solution: finish the kernel and start another
Ensure correct order of memory operations to local or global memory (with flushes or queuing a memory fence)

## Slide 128
Where might we need synchronization?
Consider a reduction … reduce a set of numbers to a single value
  E.g. find sum of all elements in an array
Sequential code
int reduce(int Ndim, int *A)
{
int sum = 0;
for (int i = 0; i < Ndim; i++)
sum += A[i];
return sum;
}

## Slide 129
Simple parallel reduction
A reduction can be carried out in three steps:
  Each work-item sums its private values into a local array indexed by the work-item’s local id
  When all the work-items have finished, one work-item sums the local array into an element of a global array (indexed by work-group id).
  When all work-groups have finished the kernel execution, the global array is summed on the host.
Note: this is a simple reduction that is straightforward to implement. More efficient reductions do the work-group sums in parallel on the device rather than on the host. These more scalable reductions are considerably more complicated to implement.

## Slide 130
A simple program that uses a reduction
Numerical Integration
Mathematically, we know that we can approximate the integral as a sum of rectangles.
Each rectangle has width and height at the middle of interval.
F(x) = 4.0/(1+x2)
4.0
2.0
1.0
X
0.0

## Slide 131
Numerical integration source code
The serial Pi program
static long num_steps = 100000;
double step;
void main()
{
int i; double x, pi, sum = 0.0;
step = 1.0/(double) num_steps;
for (i = 0; i < num_steps; i++) {
x = (i+0.5)*step;
sum = sum + 4.0/(1.0+x*x);
}
pi = step * sum;
}

## Slide 132
练习 9: The Pi program
目标：
  To understand synchronization between work-items in the OpenCL C kernel programming language
流程：
  Start with the provided serial program to estimate Pi through numerical integration
  Write a kernel and host program to compute the numerical integral using OpenCL
  Note: You will need to implement a reduction
预期输出:
  Output result plus an estimate of the error in the result
  Report the runtime
Hint: you will want each work-item to do many iterations of the loop, i.e. don’t create one work-item per loop iteration. To do so would make the reduction so costly that performance would be terrible.

## Slide 133
Heterogeneous computing with OpenCL
章节 8

## Slide 134
Running on the CPU and GPU
Kernels can be run on multiple devices at the same time
We can exploit many GPUs and the host CPU for computation
Simply define a context with multiple platforms, devices and queues
We can even synchronize between queues using Events (see appendix)
Can have more than one context
Queue
Queue
Context
GPU
CPU

## Slide 135
Running on the CPU and GPU
Discover all your platforms and devices
  Look at the API for finding out Platform and Device IDs
Set up the cl::Context with a vector of devices
cl::Context(const VECTOR_CLASS<Device> &devices,
cl_context_properties *properties = NULL,
void (CL_CALLBACK *pfn_notify)(
const char *errorinfo,
const void *private_info_size,
::size_t cb, void *user_data) = NULL,
void *user_data = NULL, cl_int *err = NULL);
Create a Command Queue for each of these devices
  C examples in the NVIDIA (oclSimpleMultiGPU) and AMD (SimpleMultiDevice) OpenCL SDKs
The steps are the same in C and Python, just the API calls differ as usual

## Slide 136
练习 10: Heterogeneous Computing
目标：
  To experiment with running kernels on multiple devices
流程：
  Take one of your OpenCL programs
  Investigate the Context constructors to include more than one device
  Modify the program to run a kernel on multiple devices, each with different input data
  Split your problem across multiple devices if you have time
  Use the examples from the SDKs to help you
预期输出:
  Output the results from both devices and see which runs faster

## Slide 137
Enabling Portable Performance via OpenCL
章节 9

## Slide 138
Portable performance in OpenCL
Portable performance is always a challenge, more so when OpenCL devices can be so varied (CPUs, GPUs, …)
But OpenCL provides a powerful framework for writing performance portable code
The following slides are general advice on writing code that should work well on most OpenCL devices

## Slide 139
Optimization issues
Efficient access to memory
  Memory coalescing
    Ideally get work-item i to access data[i] and work-item j to access data[j] at the same time etc.
  Memory alignment
    Padding arrays to keep everything aligned to multiples of 16, 32 or 64 bytes
Number of work-items and work-group sizes
  Ideally want at least 4 work-items per PE in a Compute Unit on GPUs
  More is better, but diminishing returns, and there is an upper limit
    Each work item consumes PE finite resources (registers etc)
Work-item divergence
  What happens when work-items branch?
  Actually a SIMD data parallel model
  Both paths (if-else) may need to be executed (branch divergence), avoid where possible (non-divergent branches are termed uniform)

## Slide 140
Memory layout is critical to performance
“Structure of Arrays vs. Array of Structures” problem:
struct { float x, y, z, a; } Point;
Structure of Arrays (SoA) suits memory coalescence on GPUs
Array of Structures (AoS) may suit cache hierarchies on CPUs
x | x | x | x | … | y | y | y | y | … | z | z | z | z | … | a | a | a | a | …
x | y | z | a | … | x | y | z | a | … | x | y | z | a | … | x | y | z | a | …
Adjacent work-items like to access adjacent memory
Individual work-items like to access adjacent memory

## Slide 141
Other optimisation tips
Use a profiler to see if you’re getting good performance
  Occupancy is a measure of how active you’re keeping each PE
  Occupancy measurements of >0.5 are good (>50% active)
Other measurements to consider with the profiler:
  Memory bandwidth – should aim for a good fraction of peak
    E.g. 148 GBytes/s to Global Memory on an M2050 GPU
  Work-Item (Thread) divergence – want this to be low
  Registers per Work-Item (Thread) – ideally low and a nice divisor of the number of hardware registers per Compute Unit
    E.g. 32,768 on M2050 GPUs
    These are statically allocated and shared between all Work-Items and Work-Groups assigned to each Compute Unit
    Four Work-Groups of 1,024 Work-Items each would result in just 8 registers per Work-Item! Typically aim for 16-32 registers per Work-Item

## Slide 142
Portable performance in OpenCL
Don’t optimize too hard for any one platform, e.g.
  Don’t write specifically for certain warp/wavefront sizes etc
  Be careful not to rely on specific sizes of local/global memory
  OpenCL’s vector data types have varying degrees of support – faster on some devices, slower on others
  Some devices have caches in their memory hierarchies, some don’t, and it can make a big difference to your performance without you realizing
  Choosing the allocation of Work-Items to Work-Groups and dimensions on your kernel launches
  Performance differences between unified vs. disjoint host/global memories
  Double precision performance varies considerably from device to device
  Some OpenCL SDKs give useful feedback about how well they can compile your code (but you have to turn on this feedback)
It is a good idea to try your code on several different platforms to see what happens (profiling is good!)
  At least two different GPUs (ideally different vendors) and at least one CPU

## Slide 143
Advice for performance portability
Discover what devices you have available at run-time, e.g.
// Get available platforms
cl_uint nPlatforms;
cl_platform_id platforms[MAX_PLATFORMS];
int ret = clGetPlatformIDs(MAX_PLATFORMS, platforms, &nPlatforms);
// Loop over all platforms
for (int p = 0; p < nPlatforms; p++) {
// Get available devices
cl_uint nDevices = 0;
cl_device_id devices[MAX_DEVICES];
clGetDeviceIDs(platforms[p], deviceType, MAX_DEVICES, devices, &nDevices);
// Loop over all devices in this platform
for (int d = 0; d < nDevices; d++)
getDeviceInformation(devices[d]);
}
C

## Slide 144
Advice for performance portability
Micro-benchmark all your OpenCL devices at run-time to gauge how to divide your total workload across all the devices
  Ideally use some real work so you’re not wasting resource
  Keep the microbenchmark very short otherwise slower devices penalize faster ones
Once you’ve got a work fraction per device calculated, it might be worth retesting from time to time
  The behavior of the workload may change
  The host or devices may become busy (or quiet)
It is most important to keep the fastest devices busy
  Less important if slower devices finish slightly earlier than faster ones (and thus become idle)
Avoid overloading the CPU with both OpenCL host code and OpenCL device code at the same time

## Slide 145
Timing microbenchmarks (C)
for (int i = 0; i < numDevices; i++) {
// Wait for the kernel to finish
ret = clFinish(oclDevices[i].queue);
// Update timers
cl_ulong start, end;
ret = clGetEventProfilingInfo(oclDevices[i].kernelEvent,
CL_PROFILING_COMMAND_START,
sizeof(cl_ulong), &start, NULL);
ret |= clGetEventProfilingInfo(oclDevices[i].kernelEvent,
CL_PROFILING_COMMAND_END,
sizeof(cl_ulong), &end, NULL);
long timeTaken = (end - start);
speeds[i] = timeTaken / oclDevices[i].load;
}

## Slide 146
Advice for performance portability
Optimal Work-Group sizes will differ between devices
  E.g. CPUs tend to prefer 1 Work-Item per Work-Group, while GPUs prefer lots of Work-Items per Work-Group (usually a multiple of the number of PEs per Compute Unit, i.e. 32, 64 etc.)
From OpenCL v1.1 you can discover the preferred Work-Group size multiple for a kernel once it’s been built for a specific device
  Important to pad the total number of Work-Items to an exact multiple of this
  Again, will be different per device
The OpenCL run-time will have a go at choosing good EnqueueNDRangeKernel dimensions for you
  With very variable results
Your mileage will vary, the best strategy is to write adaptive code that makes decisions at run-time

## Slide 147
Tuning Knobs some general issues to think about
Tiling size (work-group sizes, dimensionality etc.)
  For block-based algorithms (e.g. matrix multiplication)
  Different devices might run faster on different block sizes
Data layout
  Array of Structures or Structure of Arrays (AoS vs. SoA)
  Column or Row major
Caching and prefetching
  Use of local memory or not
  Extra loads and stores assist hardware cache?
Work-item / work-group data mapping
  Related to data layout
  Also how you parallelize the work
Operation-specific tuning
  Specific hardware differences
  Built-in trig / special function hardware
  Double vs. float (vs. half)
From Zhang, Sinclair II and Chien: Improving Performance Portability in OpenCL Programs – ISC13

## Slide 148
Auto tuning
Q: How do you know what the best parameter values for your program are?
  What is the best work-group size, for example
A: Try them all! (Or a well chosen subset)
This is where auto tuning comes in
  Run through different combinations of parameter values and optimize the runtime (or another measure) of your program.

## Slide 149
Auto tuning example - Flamingo
http://mistymountain.co.uk/flamingo/
Python program which compiles your code with different parameter values, and calculates the “best” combination to use
Write a simple config file, and Flamingo will run your program with different values, and returns the best combination
Remember: scale down your problem so you don’t have to wait for “bad” values (less iterations, etc.)

## Slide 150
Auto tuning - Example
D2Q9 Lattice-Boltzmann
What is the best work-group size for a specific problem size (3000x2000) on a specific device (NVIDIA Tesla M2050)?
X values
Y values
Runtimes – lower is better
Best: 60x1

## Slide 151
练习 11: Optimize matrix multiplication
目标：
  To understand portable performance in OpenCL
流程：
  Optimize a matrix multiply solution step by step, saving intermediate versions and tracking performance improvements
  After you’ve tried to optimize the program on your own, study the blocked solution optimized for an NVIDIA GPU. Apply these techniques to your own code to further optimize performance
  As a final step, go back and make a single program that is adaptive so it delivers good results on both a CPU and a GPU
预期输出:
  A message confirming that the matrix multiplication is correct
  Report the runtime and the MFLOPS

## Slide 152
Optimizing OpenCL performance
章节 10

## Slide 153
Extrae and Paraver
From Barcelona Supercomputing Center
  http://www.bsc.es/computer-sciences/performance-tools/trace-generation
  http://www.bsc.es/computer-sciences/performance-tools/paraver
Create and analyze traces of OpenCL programs
  Also MPI, OpenMP
Required versions:
  Extrae v2.3.5rc
  Paraver 4.4.5

## Slide 154
Extrae and Paraver
Extrae instruments your application and produces “timestamped events of runtime calls, performance counters and source code references”
  Allows you to measure the run times of your API and kernel calls
Paraver provides a way to view and analyze these traces in a graphical way

## Slide 155
Important!
At the moment NVIDIA® GPUs support up to OpenCL v1.1 and AMD® and Intel® support v1.2
If you want to profile on NVIDIA® devices you must compile Extrae against the NVIDIA headers and runtime otherwise v1.2 code will be used by Extrae internally which will cause the trace step to segfault

## Slide 156
Installing Extrae and Paraver
Paraver is easy to install on Linux
  Just download and unpack the binary
Extrae has some dependencies, some of which you’ll have to build from source
  libxml2
  binutils-dev
  libunwind
  PAPI
  MPI (optional)
Use something like the following command line to configure before “make && make install”:
./configure –-prefix=$HOME/extrae --with-binutils=$HOME --with-papi=$HOME --with-mpi=$HOME --without-dyninst --with-unwind=$HOME --with-opencl=/usr/local/ --with-opencl-libs=/usr/lib64

## Slide 157
Step 1 – tracing your code
Copy the trace.sh script from extrae/share/example/OPENCL to your project directory
  This sets up a few environment variables and then runs your compiled binary
Copy the extrae.xml file from the same location to your project directory
  This gives some instructions to Extrae as to how to profile your code
  Lots of options here – see their user guide
  The default they provide is fine to use to begin with
Trace!
  ./trace.sh ./a.out

## Slide 158
Step 2 – visualize the trace
Extrae produces a number of files
  .prv, .pcf, .row, etc…
Run Paraver
  ./wxparaver-<version>/bin/wxparaver
Load in the trace
  File –> Load Trace -> Select the .prv file
Load in the provided OpenCL view config file
  File -> Load configuration -> wxparaver-<version>/cfgs/OpenCL/views/opencl_call.cfg
The traces appear as three windows
  OpenCL call in host - timings of API calls
  Kernel Name – run times of kernel executions
  OpenCL call in accelerator – information about total compute vs memory transfer times

## Slide 159
Paraver

## Slide 160
Usage Tips
Show what the colours represent
  Right click -> Info Panel
Zoom in to examine specific areas of interest
  Highlight a section of the trace to populate the timeline window
Tabulate the data – numerical timings of API calls
  Select a timeline in the Paraver main window, click on the ‘New Histogram’ icon and select OK
Powerful software – can also pick up your MPI communications
Perform calculations with the data – see the Paraver user guide

## Slide 161
Platform specific profilers
More information can be obtained about your OpenCL program by profiling it using the hardware vendors dedicated profilers
OpenCL profiling can be done with Events in the API itself for specific profiling of queues and kernel calls

## Slide 162
NVIDIA Visual Profiler®
This gives us information about: Device occupancy Memory bandwidth(between host and device) | Number of registers uses Timeline of kernel executions and memory copies Etc…
第三方名称是其公司所有财产
Start a new session:
Follow the wizard, selecting the compiled binary in the File box (you do not need to make any code or compiler modifications). You can leave the other options as the default.
The binary is then run and profiled and the results displayed.

## Slide 163
Profiling using nvvp
The timeline says what happened during the program execution:
Some things to think about optimising are displayed in the Analysis tab:
Kernels
Each invocation of the kernel is pictured as a box

## Slide 164
Profiling using nvvp
The Details tab shows information for each kernel invocation and memory copy
  number of registers used
  work group sizes
  memory throughput
  amount of memory transferred
No information about which parts of the kernel are running slowly, but the figures here might give us a clue as to where to look
Best way to learn: experiment with an application yourself

## Slide 165
Profiling from the command line
NVIDIA® also have nvprof and 'Command Line Profiler’
nvprof available with CUDA™ 5.0 onwards, but currently lacks driver support for OpenCL profiling
The legacy command-line profiler can be invoked using environment variables:
$ export COMPUTE_PROFILE=1
$ export COMPUTE_PROFILE_LOG=<output file>
$ export COMPUTE_PROFILE_CONFIG=<config file>
Config file controls which events to collect (run nvprof --query-events for a comprehensive list)
Run your application to collect event information and then inspect output file with text editor
Can also output CSV information (COMPUTE_PROFILE_CSV=1) for inspection with a spreadsheet or import into nvvp (limited support)
第三方名称是其公司所有财产

## Slide 166
AMD® CodeXL
AMD provide a graphical Profiler and Debugger for AMD Radeon™ GPUs
Can give information on:
  API and kernel timings
  Memory transfer information
  Register use
  Local memory use
  Wavefront usage
  Hints at limiting performance factors
第三方名称是其公司所有财产

## Slide 167
CodeXL
Create a new project, inserting the binary location in the window
Click on the Profiling button, and hit the green arrow to run your program
Select the different traces to view associated information

## Slide 168
CodeXL
GPU: Performance Counters
  Information on kernels including work group sizes, registers, etc.
  View the kernel instruction code
    Click on the kernel name in the left most column
  View some graphs and hints about the kernel
    Click on the Occupancy result

## Slide 169
CodeXL
GPU: Application Trace
  See timing information about API calls
  Timings of memory movements
  Timings of kernel executions

## Slide 170
练习 12: Profiling OpenCL programs
目标：
  To experiment with profiling tools
流程：
  Take one of your OpenCL programs, such as matrix multiply
  Run the program in the profiler and explore the results
  Modify the program to change the performance in some way and observe the effect with the profiler
  Repeat with other programs if you have time
预期输出:
  Timings reported by the host code and via the profiling interfaces should roughly match

## Slide 171
Debugging OpenCL
章节 11

## Slide 172
Debugging OpenCL
Parallel programs can be challenging to debug
Luckily there are some tools to help
Firstly, if your device can run OpenCL 1.2, you can printf straight from the kernel.
Here, each work-item will print to stdout
Note: there is some buffering between the device and the output, but will be flushed by calling clFinish (or equivalent)
__kernel void func(void)
{
int i = get_global_id(0);
printf(" %d\n ", i);
}

## Slide 173
Debugging OpenCL 1.1
Top tip:
  Write data to a global buffer from within the kernel
result[ get_global_id(0) ] = … ;
  Copy back to the host and print out from there or debug as a normal serial application
Works with any OpenCL device and platform

## Slide 174
Debugging OpenCL – more tips
Check your error messages!
  If you enable Exceptions in C++ as we have here, make sure you print out the errors.
Don’t forget, use the err_code.c from the tutorial to print out errors as strings (instead of numbers), or check in the cl.h file in the include directory of your OpenCL provider for error messages
Check your work-group sizes and indexing

## Slide 175
Debugging OpenCL - GDB
Can also use GDB to debug your programs on the CPU
  This will also leverage the memory system
    Might catch illegal memory dereferences more accurately
  But it does behave differently to accelerator devices so bugs may show up in different ways
As with debugging, compile your C or C++ programs with the –g flag

## Slide 176
Debugging OpenCL - GDB
Require platform specific instructions depending on if you are using the AMD® or Intel® OpenCL platform
  This is in part due to the ICD (Installable Client Driver) ensuring that the correct OpenCL runtime is loaded for the chosen platform
  Also different kernel compile flags are accepted/required by different OpenCL implementations
Remember: your CPU may be listed under each platform – ensure you choose the right debugging method for the platform
第三方名称是其公司所有财产

## Slide 177
Using GDB with AMD®
Ensure you select the CPU device from the AMD® platform
Must use the –g flag and turn off all optimizations when building the kernels:
program.build(" –g –O0" )
The symbolic name of a kernel function “__kernel void foo(args)” is “__OpenCL_foo_kernel”
  To set a breakpoint on kernel entry enter at the GDB prompt:
break __OpenCL_foo_kernel
Note: the debug symbol for the kernel will not show up until the kernel has been built by your host code
AMD® recommend setting the environment variable CPU_MAX_COMPUTE_UNITS=1 to ensure deterministic kernel behaviour
第三方名称是其公司所有财产

## Slide 178
Using GDB with Intel®
Ensure you select the CPU device from the Intel® platform
Must use the –g flag and specify the kernel source file when building the kernels:
program.build(" –g –s /full/path/to/kernel.cl" )
The symbolic name of a kernel function “__kernel void foo(args)” is “foo”
  To set a breakpoint on kernel entry enter at the GDB prompt:
break foo
Note: the debug symbol for the kernel will not show up until the kernel has been built by your host code
第三方名称是其公司所有财产

## Slide 179
Debugging OpenCL – Using GDB
Use n to move to the next line of execution
Use s to step into the function
If you reach a segmentation fault, backtrace lists the previous few execution frames
  Type frame 5 to examine the 5th frame
Use print varname to output the current value of a variable

## Slide 180
Oclgrind
A SPIR interpreter and OpenCL simulator
Developed at the University of Bristol
Runs OpenCL kernels in a simulated environment to catch various bugs:
  oclgrind ./application
  Invalid memory accesses
  Data-races (--data-races)
  Work-group divergence
  Runtime API errors (--check-api)
Also has a GDB-style interactive debugger
  oclgrind –i ./application
More information on the Oclgrind Website

## Slide 181
GPUVerify
A useful tool for detecting data-races in OpenCL programs
Developed at Imperial College as part of the CARP project
Uses static analysis to try to prove that kernels are free from races
Can also detect issues with work-group divergence
More information on the GPUVerify Website
gpuverify --local_size=64,64 --num_groups=256,256 kernel.cl

## Slide 182
Other debugging tools
AMD® CodeXL
  For AMD® APUs, CPUs and GPUs
    Graphical Profiler and Debugger
NVIDIA® Nsight™ Development Platform
  For NVIDIA® GPUs
    IDE, including Profiler and Debugger
GPUVerify
  Formal analysis of kernels
  http://multicore.doc.ic.ac.uk/tools/GPUVerify/
第三方名称是其公司所有财产
Note: Debugging OpenCL is still changing rapidly - your mileage may vary when using GDB and these tools

## Slide 183
Porting CUDA to OpenCL
章节 12

## Slide 184
Introduction to OpenCL
If you have CUDA code, you’ve already done the hard work!
  I.e. working out how to split up the problem to run effectively on a many-core device
Switching between CUDA and OpenCL is mainly changing the host code syntax
  Apart from indexing and naming conventions in the kernel code (simple to change!)

## Slide 185
Memory Hierarchy Terminology
CUDA
OpenCL
Private – within a work-item
Local – within a thread
Local – shared between work-items in a work-group
Shared – shared between threads in a thread block
Constant – a cache for constant memory
Constant – a cache for constant memory
Device – shared between all thread blocks
Global – shared between all work-groups

## Slide 186
Allocating and copying memory
 | CUDA C | OpenCL C
Allocate | float* d_x; cudaMalloc(&d_x, sizeof(float)*size); | cl_mem d_x = clCreateBuffer(context, CL_MEM_READ_WRITE, sizeof(float)*size, NULL, NULL);
Host to Device | cudaMemcpy(d_x, h_x, sizeof(float)*size, cudaMemcpyHostToDevice); | clEnqueueWriteBuffer(queue, d_x, CL_TRUE, 0, sizeof(float)*size, h_x, 0, NULL, NULL);
Device to Host | cudaMemcpy(h_x, d_x, sizeof(float)*size, cudaMemcpyDeviceToHost); | clEnqueueReadBuffer(queue, d_x, CL_TRUE, 0, sizeof(float)*size, h_x, 0, NULL, NULL);

## Slide 187
Allocating and copying memory
 | CUDA C | OpenCL C++
Allocate | float* d_x; cudaMalloc(&d_x, sizeof(float)*size); | cl::Buffer d_x(begin(h_x), end(h_x), true);
Host to Device | cudaMemcpy(d_x, h_x, sizeof(float)*size, cudaMemcpyHostToDevice); | cl::copy(begin(h_x), end(h_x), d_x);
Device to Host | cudaMemcpy(h_x, d_x, sizeof(float)*size, cudaMemcpyDeviceToHost); | cl::copy(d_x, begin(h_x), end(h_x));

## Slide 188
Declaring dynamic local/shared memory
CUDA C
Define an array in the kernel source as extern
__shared__ int array[];
When executing the kernel, specify the third parameter as size in bytes of shared memory
func<<<num_blocks,
num_threads_per_block,
shared_mem_size>>>(args);
OpenCL C++
Have the kernel accept a local array as an argument
__kernel void func(
__local int *array)
{}
Define a local memory kernel kernel argument of the right size
cl::LocalSpaceArg localmem =
cl::Local(shared_mem_size);
Pass the argument to the kernel invocation
func(EnqueueArgs(…),localmem);

## Slide 189
Declaring dynamic local/shared memory
CUDA C
Define an array in the kernel source as extern
__shared__ int array[];
When executing the kernel, specify the third parameter as size in bytes of shared memory
func<<<num_blocks,
num_threads_per_block,
shared_mem_size>>>(args);
OpenCL C
Have the kernel accept a local array as an argument
__kernel void func(
__local int *array) {}
Specify the size by setting the kernel argument
clSetKernelArg(kernel, 0,
sizeof(int)*num_elements,
NULL);

## Slide 190
Dividing up the work
To enqueue the kernel
  CUDA – specify the number of thread blocks and threads per block
  OpenCL – specify the problem size and (optionally) number of work-items per work-group
Problem size
CUDA
OpenCL
Work-item
Thread
Thread block
Work-group

## Slide 191
Enqueue a kernel (C)
CUDA C
dim3 threads_per_block(30,20);
dim3 num_blocks(10,10);
kernel<<<num_blocks,
threads_per_block>>>();
OpenCL C
const size_t global[2] =
{300, 200};
const size_t local[2] =
{30, 20};
clEnqueueNDRangeKernel(
queue, &kernel,
2, 0, &global, &local,
0, NULL, NULL);

## Slide 192
Enqueue a kernel (C++)
CUDA C
dim3 threads_per_block(30,20);
dim3 num_blocks(10,10);
kernel<<<num_blocks,
threads_per_block>>>(…);
OpenCL C++
const cl::NDRange global(300, 200);
const cl::NDRange local(30, 20);
kernel(
EnqueueArgs(global, local),
…);

## Slide 193
Indexing work
CUDA
gridDim
blockIdx
blockDim
gridDim * blockDim
threadIdx
blockIdx * blockdim + threadIdx
OpenCL
get_num_groups()
get_group_id()
get_local_size()
get_global_size()
get_local_id()
get_global_id()

## Slide 194
Differences in kernels
Where do you find the kernel?
  OpenCL - either a string (const char *), or read from a file
  CUDA – a function in the host code
Denoting a kernel
  OpenCL - __kernel
  CUDA - __global__
When are my kernels compiled?
  OpenCL – at runtime
  CUDA – with compilation of host code

## Slide 195
Host code
By default, CUDA initializes the GPU automatically
  If you needed anything more complicated (multi-device etc.) you must do so manually
OpenCL always requires explicit device initialization
  It runs not just on NVIDIA® GPUs and so you must tell it which device(s) to use
第三方名称是其公司所有财产

## Slide 196
Thread Synchronization
CUDA | OpenCL
__syncthreads() | barrier()
__threadfenceblock() | mem_fence( CLK_GLOBAL_MEM_FENCE ¦ CLK_LOCAL_MEM_FENCE)
No equivalent | read_mem_fence()
No equivalent | write_mem_fence()
__threadfence() | Finish one kernel and start another

## Slide 197
Translation from CUDA to OpenCL
CUDA | OpenCL
GPU | Device (CPU, GPU etc)
Multiprocessor | Compute Unit, or CU
Scalar or CUDA core | Processing Element, or PE
Global or Device Memory | Global Memory
Shared Memory (per block) | Local Memory (per workgroup)
Local Memory (registers) | Private Memory
Thread Block | Work-group
Thread | Work-item
Warp | No equivalent term (yet)
Grid | NDRange

## Slide 198
More information
http://developer.amd.com/Resources/hc/OpenCLZone/programming/pages/portingcudatoopencl.aspx

## Slide 199
练习 13: Porting CUDA to OpenCL
目标：
  To port the provided CUDA/serial C program to OpenCL
流程：
  Examine the CUDA kernel and identify which parts need changing
    Change them to the OpenCL equivalents
  Examine the Host code and port the commands to the OpenCL equivalents
预期输出:
  The OpenCL and CUDA programs should produce the same output – check this!

## Slide 200
Some Concluding remarks

## Slide 201
Conclusion
OpenCL has widespread industrial support
OpenCL defines a platform-API/framework for heterogeneous computing, not just GPGPU or CPU-offload programming
OpenCL has the potential to deliver portably performant code; but it has to be used correctly
The latest C++ and Python APIs make developing OpenCL programs much simpler than before
The future is clear:
  OpenCL is the only parallel programming standard that enables mixing task parallel and data parallel code in a single program while load balancing across ALL of the platform’s available resources.

## Slide 202
Other important related trends
OpenCL’s Standard Portable Intermediate Representation (SPIR)
  Based on LLVM’s IR
  Makes interchangeable front- and back-ends straightforward
  Now libraries of OpenCL kernels can be distributed in "binary" form, protecting software developer IP
OpenCL 2.0 adds support for:
  Shared virtual memory to share addresses between the host and the devices
  Dynamic (nested) parallelism, enabling kernels to directly enqueue other kernels on the same device without host intervention
  A formal memory model based on C11
  A generic address space to enable easier mixing and matching between host/global/local/private
  Pipes as memory objects
  Sub-groups to expose warp/wavefront-like hardware features
  Lots of other improvements!
For the latest news on SPIR and new OpenCL versions see:
  http://www.khronos.org/opencl/
第三方名称是其公司所有财产

## Slide 203
Resources: https://www.khronos.org/opencl/
OpenCL Programming Guide:
Aaftab Munshi, Benedict Gaster, Timothy G. Mattson and James Fung, 2011
Heterogeneous Computing with OpenCL
Benedict Gaster, Lee Howes, David R. Kaeli, Perhaad Mistry and Dana Schaa, 2011
The OpenCL specification
Surprisingly approachable for a spec!
https://www.khronos.org/registry/cl/
OpenCL reference card
Useful to have on your desk(top)
Available on the same page as the spec.

## Slide 204
Other OpenCL resources
New annual OpenCL conference
  http://www.iwocl.org/
  Held in May each year
  CFP to be announced at SC
OpenCL Forums:
  Khronos' OpenCL forums are the central place to be:
  http://www.khronos.org/message_boards/forumdisplay.php?f=61

## Slide 205
Other OpenCL resources
CLU: a library of useful C-level OpenCL utilities, such as program initialization, CL kernel code compilation and calling kernels with their arguments (bit like GLUT!):https://github.com/Computing-Language-Utility/CLU
clMath: an open source BLAS / FFT library originally developed by AMDhttps://github.com/clMathLibraries/clBLAS and https://github.com/clMathLibraries/clFFT

## Slide 206
Versions of opencl

## Slide 207
OpenCL 1.0
First public release, December 2008

## Slide 208
OpenCL 1.1
Released June 2010
Major new features:
  Sub buffers
  User events
  More built-in functions
  32-bit atomics become core features

## Slide 209
OpenCL 1.2
Released November 2011
Major new features:
  Custom devices and built-in kernels
  Device partitioning
  Support separate compilation and linking of programs
  Greater support for OpenCL libraries

## Slide 210
OpenCL 2.0
Released in November 2013
Major new features:
  Shared virtual memory (SVM)
  Dynamic parallelism
  Pipes
  Built-in reductions/broadcasts
  Sub-groups
  "generic" address space
  C11 atomics
  More image support

## Slide 211
Vector operations within kernels
Appendix A

## Slide 212
Before we continue...
The OpenCL device compilers are good at auto-vectorising your code
  Adjacent work-items may be packed to produce vectorized code
By using vector operations the compiler may not optimize as sucessfully
So think twice before you explicitly vectorize your OpenCL kernels, you might end up hurting performance!

## Slide 213
Vector operations
Modern microprocessors include vector units:
Functional units that carry out operations on blocks of numbers
For example, x86 CPUs have over the years introduced MMX, SSE, and AVX instruction sets …
characterized in part by their widths (e.g. SSE operates on 128 bits at a time, AVX 256 bits etc)
To gain full performance from these processors it is important to exploit these vector units
Compilers can sometimes automatically exploit vector units.
Experience over the years has shown, however, that you all too often have to code vector operations by hand.
Example using 128 bit wide SSE:
#include "xmmintrin.h " // vector intrinsics from gcc for SSE (128 bit wide)
__m128 ramp = _mm_setr_ps(0.5, 1.5, 2.5, 3.5); // pack 4 floats into vector register
__m128 vstep = _mm_load1_ps(&step); // pack step into a vector register
__m128 xvec; = _mm_mul_ps(ramp,vstep); // multiple corresponding 32 bit
// floats and assign to xvec

## Slide 214
Vector intrinsics challenges
Requires an assembly code style of programming:
  Load into registers
  Operate with register operands to produce values in another vector register
Non portable
  Change vector instruction set (even from the same vendor) and code must be re-written. Compilers might treat them differently too
Consequences:
  Very few programmers are willing to code with intrinsics
  Most programs only exploit vector instructions that the compiler can automatically generate – which can be hit or miss
  Most programs grossly under exploit available performance.
Solution: a high level portable vector instruction set … which is precisely what OpenCL provides.

## Slide 215
Vector Types
The OpenCL C kernel programming language provides a set of vector instructions:
  These are portable between different vector instruction sets
These instructions support vector lengths of 2, 4, 8, and 16 … for example:
  char2, ushort4, int8, float16, double2, …
Properties of these types include:
  Endian safe
  Aligned at vector length
  Vector operations (elementwise) and built-in functions
Remember, double (and hence vectors of double) are optional in OpenCL v1.1

## Slide 216
Vector Operations
Vector literal
Vector components
Vector ops
int4 vi0 = (int4) -7;
int4 vi1 = (int4) (0, 1, 2, 3);
vi0.lo = vi1.hi;
int8 v8 = (int8) (vi0, vi1.s01, vi1.odd);
vi0 += vi1;
vi0 = abs(vi0);
-7 | -7 | -7 | -7
0 | 1 | 2 | 3
2 | 3 | -7 | -7
2 | 3 | -7 | -7 |  |  |  | 
0 | 1
1 | 3
2 | 3 | -7 | -7
0 | 1 | 2 | 3
2 | 4 | -5 | -4
+
2 | 4 | 5 | 4

## Slide 217
Using vector operations
You can convert a scalar loop into a vector loop using the following steps:
  Based on the width of your vector instruction set and your problem, choose the number of values you can pack into a vector register (the width):
    E.g. for a 128 bit wide SSE instruction set and float data (32 bit), you can pack four values (128 bits =4*32 bits) into a vector register
  Unroll the loop to match your width (in our example, 4)
  Set up the loop preamble and postscript. For example, if the number of loop iterations doesn’t evenly divide the width, you’ll need to cover the extra iterations in a loop postscript or pad your vectors in a preamble
  Replace instructions in the body of the loop with their vector instruction counter parts

## Slide 218
Vector instructions example
Scalar loop:
for (i = 0; i < 34; i++) x[i] = y[i] * y[i];
Width for a 128-bit SSE is 128/32=4
Unroll the loop, then add postscript and premable as needed:
NLP = 34+2; x[34]=x[35]=y[34]=y[35]=0.0f // preamble to zero pad
for (i = 0; i < NLP; i = i + 4) {
x[i] = y[i] * y[i]; x[i+1] = y[i+1] * y[i*1];
x[i+2] = y[i+2] * y[i*2]; x[i+3] = y[i+3] * y[i*3];
}
Replace unrolled loop with associated vector instructions:
float4 x4[DIM], y4[DIM];
// DIM set to hold 34 values extended to multiple of 4 (36)
float4 zero = {0.0f, 0.0f, 0.0f, 0.0f};
NLP = 34 % 4 + 1; // 9 values (as 34 isn’t a multiple of 4)
x4[NLP-1] = 0.0f; y4[NLP-1] = 0.0f; // zero pad arrays
for (i = 0; i < NLP; i++)
x4[i] = y4[i] * y4[i]; // actual vector operations

## Slide 219
练习 A: The vectorized Pi program
目标：
  To understand the vector instructions in the kernel programming language
流程：
  Start with your best Pi program
  Unroll the loops 4 times. Verify that the program still works
  Use vector instructions in the body of the loop
预期输出:
  Output result plus an estimate of the error in the result
  Report the runtime and compare vectorized and scalar versions of the program
  You could try running this on the CPU as well as the GPU…

## Slide 220
The OpenCL event model
Appendix B

## Slide 221
OpenCL Events
An event is an object that communicates the status of commands in OpenCL … legal values for an event:
  CL_QUEUED: command has been enqueued.
  CL_SUBMITTED: command has been submitted to the compute device
  CL_RUNNING: compute device is executing the command
  CL_COMPLETE: command has completed
  ERROR_CODE: a negative value indicates an error condition occurred.
Can query the value of an event from the host … for example to track the progress of a command.
cl_int clGetEventInfo (
cl_event event, cl_event_info param_name,
size_t param_value_size, void *param_value,
size_t *param_value_size_ret)
Examples:
CL_EVENT_CONTEXT
CL_EVENT_COMMAND_EXECUTION_STATUS
CL_EVENT_COMMAND_TYPE

## Slide 222
Generating and consuming events
Consider the command to enqueue a kernel. The last three arguments optionally expose events (NULL otherwise).
cl_int clEnqueueNDRangeKernel (
cl_command_queue command_queue,
cl_kernel kernel,
cl_uint work_dim,
const size_t *global_work_offset,
const size_t *global_work_size,
const size_t *local_work_size,
cl_uint num_events_in_wait_list,
const cl_event *event_wait_list,
cl_event *event)
Pointer to an event object generated by this command
Array of pointers to the events being waited upon … Command queue and events must share a context.
Number of events this command is waiting to complete before executing

## Slide 223
Event: basic event usage
Events can be used to impose order constraints on kernel execution.
Very useful with out-of-order queues.
cl_event k_events[2];
err = clEnqueueNDRangeKernel(commands, kernel1, 1,
NULL, &global, &local, 0, NULL, &k_events[0]);
err = clEnqueueNDRangeKernel(commands, kernel2, 1,
NULL, &global, &local, 0, NULL, &k_events[1]);
err = clEnqueueNDRangeKernel(commands, kernel3, 1,
NULL, &global, &local, 2, k_events, NULL);
Enqueue two kernels that expose events
Wait to execute until two previous events complete
Notes: 223

## Slide 224
OpenCL synchronization: queues & events
Events connect command invocations. Can be used to synchronize executions inside out-of-order queues or between queues
Example: 2 queues with 2 devices
GPU
CPU
GPU
CPU
Time
Time
Kernel 1
Kernel 2
Enqueue Kernel 1
Enqueue Kernel 2
Kernel 2 starts before the results from Kernel 1 are ready
Kernel 1
Kernel 2
Enqueue Kernel 1
Enqueue Kernel 2
Kernel 2 waits for an event from Kernel 1 and does not start until the results are ready

## Slide 225
Why Events? Won’t a barrier do?
A barrier defines a synchronization point … commands following a barrier wait to execute until all prior enqueued commands complete
cl_int clEnqueueBarrier(cl_command_queue queue)
Events provide fine grained control … this can really matter with an out-of-order queue.
Events work between commands in the different queues … as long as they share a context
Events convey more information than a barrier … provide info on state of a command, not just whether it’s complete or not.
Queue
Queue
Context
GPU
CPU
Event

## Slide 226
Barriers between queues: clEnqueueBarrier doesn’t work
clEnqueueNDRangeKernel()
clEnqueueWriteBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer()
clEnqueueReadBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer()
clEnqueueNDRangeKernel()
clEnqueueWriteBuffer()
clEnqueueWriteBuffer()
clEnqueueReadBuffer()
clEnqueueReadBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer() clEnqueueNDRangeKernel()
1st Command Queue
2nd Command Queue
clEnqueueBarrier()
clEnqueueBarrier()
clEnqueueNDRangeKernel()
clEnqueueWriteBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer()
clEnqueueReadBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer()
clEnqueueNDRangeKernel()
clEnqueueWriteBuffer()
clEnqueueWriteBuffer()
clEnqueueReadBuffer()
clEnqueueReadBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer() clEnqueueNDRangeKernel()

## Slide 227
Barriers between queues: this works!
clEnqueueNDRangeKernel()
clEnqueueWriteBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer()
clEnqueueReadBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer()
clEnqueueNDRangeKernel()
clEnqueueWriteBuffer()
clEnqueueWriteBuffer()
clEnqueueReadBuffer()
clEnqueueReadBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer() clEnqueueNDRangeKernel()
1st Command Queue
2nd Command Queue
clEnqueueBarrier()
clEnqueueWaitForEvent(event)
clEnqueueMarker(event)
clEnqueueNDRangeKernel()
clEnqueueWriteBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer()
clEnqueueReadBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer()
clEnqueueNDRangeKernel()
clEnqueueWriteBuffer()
clEnqueueWriteBuffer()
clEnqueueReadBuffer()
clEnqueueReadBuffer()
clEnqueueWriteBuffer()
clEnqueueNDRangeKernel()
clEnqueueReadBuffer() clEnqueueNDRangeKernel()

## Slide 228
Host generated events influencing execution of commands: User events
“user code” running on a host thread can generate event objects
cl_event clCreateUserEvent(cl_context context, cl_int *errcode_ret)
Created with value CL_SUBMITTED.
It’s just another event to enqueued commands.
Can set the event to one of the legal event values
cl_int clSetUserEventStatus(cl_event event, cl_int execution_status)
Example use case: Queue up block of commands that wait on user input to finalize state of memory objects before proceeding.

## Slide 229
Command generated events influencing execution of host code
A thread running on the host can pause waiting on a list of events to complete. This can be done with the function:
cl_int clWaitForEvents(
cl_uint num_events,
const cl_event *event_list)
Example use case: Host code waiting for an event to complete before extracting information from the event.
Number of events to wait on
An array of pointers to event object

## Slide 230
Profiling with Events
OpenCL is a performance oriented language … Hence performance analysis is an essential part of OpenCL programming.
The OpenCL specification defines a portable way to collect profiling data.
Can be used with most commands placed on the command queue … includes:
  Commands to read, write, map or copy memory objects
  Commands to enqueue kernels, tasks, and native kernels
  Commands to Acquire or Release OpenGL objects
Profiling works by turning an event into an opaque object to hold timing data.

## Slide 231
Using the Profiling interface
Profiling is enabled when a queue is created with the CL_QUEUE_PROFILING_ENABLE flag set.
When profiling is enabled, the following function is used to extract the timing data
cl_int clGetEventProfilingInfo(
cl_event event,
cl_profiling_info param_name,
size_t param_value_size,
void *param_value,
size_t *param_value_size_ret)
Expected and actual size of profiling data.
Profiling data to query (see next slide)
Pointer to memory to hold results

## Slide 232
cl_profiling_info values
CL_PROFILING_COMMAND_QUEUED
  the device time in nanoseconds when the command is enqueued in a command-queue by the host. (cl_ulong)
CL_PROFILING_COMMAND_SUBMIT
  the device time in nanoseconds when the command is submitted to compute device. (cl_ulong)
CL_PROFILING_COMMAND_START
  the device time in nanoseconds when the command starts execution on the device. (cl_ulong)
CL_PROFILING_COMMAND_END
  the device time in nanoseconds when the command has finished execution on the device. (cl_ulong)

## Slide 233
Profiling Examples
cl_event prof_event;
cl_command_queue comm;
comm = clCreateCommandQueue(
context, device_id,
CL_QUEUE_PROFILING_ENABLE,
&err);
err = clEnqueueNDRangeKernel(
comm, kernel,
nd, NULL, global, NULL,
0, NULL, prof_event);
clFinish(comm);
err = clWaitForEvents(1, &prof_event );
cl_ulong start_time, end_time;
size_t return_bytes;
err = clGetEventProfilingInfo(
prof_event,
CL_PROFILING_COMMAND_QUEUED,
sizeof(cl_ulong),
&start_time,
&return_bytes);
err = clGetEventProfilingInfo(
prof_event,
CL_PROFILING_COMMAND_END,
sizeof(cl_ulong),
&end_time,
&return_bytes);
run_time =(double)(end_time - start_time);

## Slide 234
Events inside Kernels … Async. copy
// A, B, C kernel args … global buffers.
// Bwrk is a local buffer
for(k=0;k<Pdim;k++)
Awrk[k] = A[i*Ndim+k];
for(j=0;j<Mdim;j++){
event_t ev_cp = async_work_group_copy(
(__local float*) Bwrk, (__global float*) B,
(size_t) Pdim, (event_t) 0);
wait_group_events(1, &ev_cp);
for(k=0, tmp= 0.0;k<Pdim;k++)
tmp += Awrk[k] * Bwrk[k];
C[i*Ndim+j] = tmp;
}
Compute a row of C = A * B
  1 A col.per work-item
  Work group shares rows of B
Start an async. copy for row of B returning an event to track progress.
Wait for async. copy to complete before proceeding.
Compute element of C using A from private memory and B from local memory.

## Slide 235
Events and the C++ interface (for profiling)
Enqueue the kernel with a returned event
Event event =
vadd(
EnqueueArgs(commands,NDRange(count), NDRange(local)),
a_in, b_in, c_out, count);
What for the command attached to the event to complete
event.wait();
Extract timing data from the event:
cl_ulong ev_start_time =
event.getProfilingInfo<CL_PROFILING_COMMAND_START>();
cl_ulong ev_end_time =
event.getProfilingInfo<CL_PROFILING_COMMAND_END>();

## Slide 236
Pinned memory
Appendix C

## Slide 237
Pinned Memory
In general, the fewer transfers you can do between host and device, the better
But some are unavoidable
It is possible to speed up these transfers, by using pinned memory (also called page-locked memory)
If supported, can enable much faster host <-> device communications

## Slide 238
Pinned Memory
A regular enqueueRead/enqueueWrite command might manage ~6GB/s
But PCI-E Gen 3.0 can sustain transfer rates of up to 16GB/s
So, where has our bandwidth gone?
The operating system
Why? Let's consider when memory is actually allocated…

## Slide 239
Malloc Recap
Consider a laptop which has 16GB of RAM.
What is the output of the code on the right if run on this laptop?
Bonus Question: if compiled with –m32, what will the output be?
#include <stdlib.h>
#include <stdio.h>
int
main
(int argc, char **argv)
{
//64 billion floats
size_t len = 64 * 1024*1024*1024;
//256GB allocation
float *buffer = malloc(len*sizeof(float));
if (NULL == buffer)
{
fprintf(stderr, "malloc failed\n");
return 1;
}
printf("got ptr %p\n", buffer);
return 0;
}

## Slide 240
% gcc test.c -o test
% ./test
got ptr 0x7f84b0c03350

## Slide 241
Malloc Recap
A non-NULL pointer was returned
Both OS X and Linux will oversubscribe memory
When will this memory actually get allocated?
Checking the return value of malloc/calloc is useless – malloc never* returns NULL!
#include <stdlib.h>
#include <stdio.h>
int
main
(int argc, char **argv)
{
//64 billion floats
size_t len = 64 * 1024*1024*1024;
//256GB allocation
float *buffer = malloc(len*sizeof(float));
if (NULL == buffer)
{
fprintf(stderr, "malloc failed\n");
return 1;
}
printf("got ptr %p\n", buffer);
return 0;
}
* This might not be true for an embedded system

## Slide 242
Malloc Recap
This program does not actually allocate any memory
We call malloc, but we never use it!
#include <stdlib.h>
#include <stdio.h>
int
main
(int argc, char **argv)
{
size_t len = 16 * 1024*1024;
float *buffer = malloc(len*sizeof(float));
return 0;
}

## Slide 243
Malloc Recap
So what happens here?
The pointer we got back, when accessed, will trigger a page fault in the kernel.
The kernel will then allocate us some memory, and allow us to write to it.
But how much was allocated in this code? Only 4096 bytes (one page)
#include <stdlib.h>
#include <stdio.h>
int
main
(int argc, char **argv)
{
size_t len = 16 * 1024*1024;
float *buffer = malloc(len*sizeof(float));
buffer[0] = 10.0f;
return 0;
}

## Slide 244
Malloc Recap
4KB pages will be allocated at a time, and can also be swapped to disk dynamically
In fact, an allocation may not even be contiguous
So, enqueueRead/enqueueWrite must incur an additional host memory to host memory copy, wasting bandwidth and costing performance

## Slide 245
EnqueueWrite:
  Allocate contiguous portion of DRAM
  Copy host data into this contiguous memory
  Signal the DMA engines to start the transfer
EnqueueRead:
  Allocate contiguous portion of DRAM
  Signal DMA engine to start transfer
  Wait for interrupt to signal that the transfer has finished
  Copy transferred data from the contiguous memory into memory in the host code’s address space

## Slide 246
Pinned memory side-steps this issue by giving the host process direct access to the portions of host memory that the DMA engines read and write to.
This results in much less time spent waiting for transfers!
Disclaimer: Not all drivers support it, and it makes allocations much more expensive (so it would be slow to continually allocate and free pinned memory!)

## Slide 247
Using Pinned Memory
OpenCL has no official support for pinned memory
But e.g. NVIDIA supports pinned memory allocations (CL_MEM_ALLOC_HOST_PTR flag)
When you allocate a cl_mem object, you also allocate page-locked host memory of the same size
But this does not return the host pointer
Reading and writing data is handled by enqueueMapBuffer, which does return the host pointer
Eventually call clEnqueueUnmapMemObject when you're done
//create device buffer
cl_mem devPtrA = clCreateBuffer(
context,
CL_MEM_ALLOC_HOST_PTR, //pinned memory flag
len,
NULL, //host pointer must be NULL
NULL
);
float *hostPtrA =
(float *) clEnqueueMapBuffer(
queue,
devPtrA,
CL_TRUE, //blocking map
CL_MAP_WRITE_INVALIDATE_REGION, //write data
0, //offset of region
len, //amount of data to be mapped
0, NULL, NULL, //event information
NULL //error code pointer
);
CL_MAP_WRITE_INVALIDATE_REGION is a v1.2 feature; if using v1.1 or earlier, would have to use CL_MAP_WRITE instead.
Notes: Also relevant for zero copy etc in presence of shared memory
247

## Slide 248
Caveats
Again, allocating pinned memory is much more expensive (about 100x slower) than regular memory, so frequent allocations will be bad for performance.
However, frequent reads and writes will be much faster!
Not all platforms support pinned memory. But, the above method will still work, and at least will not be any slower than regular use

## Slide 249
C++ for C Programmers
Appendix D

## Slide 250
C++ for C programmers
This Appendix shows and highlights some of the basic features and principles of C++.
It is intended for the working C programmer.
The C++ standards:
  ISO/ANSI Standard 1998 (revision 2003)
  ISO/ANSI Standard 2011 (aka C++0x or C++11)

## Slide 251
Comments, includes, and variable definitions
Single line comments:
// this is a C++ comment
C includes are prefixed with “c”:
#include <cstdio>
IO from keyboard and to console
#include <iosteam>
int a;
std::cin >> a; // input integer to ‘a’
std::cout << a; // outputs ‘a’ to console

## Slide 252
Namespaces
Definitions and variables can be scoped with namespaces.
:: is used to dereference.
Using namespace opens names space into current scope.
Default namespace is std.
#include <iostream> // definitions in std namespace
namespace foo {
int id(int x) { return x; }
};
int x = foo::id(10);
using namespace std;
cout << x; // no need to prefix with std::

## Slide 253
References in C++ … a safer way to do pointers
References are non-null pointers. Since they can’t be NULL, you don’t have to check for NULL value all the time (as you do with C)
For example, in C we need to write:
int foo(int * x) {
if (x != NULL) return *x;
else return 0;
}
In C++ we could write:
int foo(int & x) {
return x;
}
Note that in both cases the memory address of x is passed (i.e. by reference) and not the value!

## Slide 254
New/Delete Memory allocation
C++ provides safe(r) memory allocation
new and delete operator are defined for each type, including user defined types. No need to multiple by sizeof(type) as in C.
int * x = new int;
delete x;
For multi element allocation (i.e. arrays) we must use delete[].
int * array = new int[100];
delete[] array;

## Slide 255
Overloading
C++ allows functions to have the same name but with different argument types.
int add(int x, int y)
{
return x+y;
}
float add(float x, float y)
{
return x+y;
}
// call the float version of add
float f = add(10.4f, 5.0f);
// call the int version of add
int i = add(100,20);

## Slide 256
Classes (and structs)
C++ classes are an extension of C structs (and unions) that can functions (called member functions) as well as data.
The keyword “const” can be applied to member functions such as getX() to state that the particular member function will not modify the internal state of the object, i.e it will not cause any visual effects to someone owning a pointer to the said object. This allows for the compiler to report errors if this is not the case, better static analysis, and to optimize uses of the object , i.e. promote it to a register or set of registers.
class Vector {
private:
int x_, y_, z_ ;
public:
Vector (int x, int y, int z) : x_(x), y_(y), z_(z) {} // constructor
~Vector // destructor
{
cout << “vector destructor”;
}
int getX() const { return x_; } // access member function
…
};

## Slide 257
More information about constructors
Consider the constructor from the previous slide …
Vector (int x, int y, int z): x_(x), y_(y), z_(z) {}
C++ member data local to a class (or struct) can be initialized using the noation
: data_name(initializer_name), ...
Consider the following two semantically equivalent structs in which the constructor sets the data member x_ to the input value x:
Case B must use a temporary to read the value of x, while this is not so for Case A. This is due to C’s definition of local stack allocation.
This turns out to be very import in C++11 with its memory model which states that an object is said to exist once inside the body of the constructor and hence thread safety becomes an issue, this is not the case for the constructor initalization list (case A). This means that safe double locking and similar idioms can be implemented using this approach.
struct Foo
{
int x_;
Foo(int x) : x_(x) {}
}
struct Foo
{
int x_;
Foo(int x) { x_ = x; }
}
A
B

## Slide 258
Classes (and structs) continued
Consider the following block where we construct an object (the vector “v”), use it and then reach the end of the block
{
Vector v(10,20,30);
// vector {x_ = 10, y_ = 20 , z_ = 30}
// use v
} // at this point v’s destructor would be called!
Note that at the end of the block, v is no longer accessible and hence can be destroyed. At this point, the destructor for v is called.

## Slide 259
Classes (and structs) continued
There is a lot more to classes, e.g. inheritance but it is all based on this basic notion.
The previous examples adds no additional data or overhead to a traditional C struct, it has just improved software composibility.

## Slide 260
Function objects
Function application operator can be overloaded to define functor classes
struct Functor
{
int operator() (int x) { return x*x; }
};
// create an object of type Functor
Functor f();
int value = f(10); // call the operator()

## Slide 261
Template functions
Don’t want to write the same function many times for different types?
Templates allow functions to be parameterized with a type(s).
template<typename T>
T add(T x, T y) { return x+y; }
float f = add<float>(10.4f, 5.0f); // float version
int i = add<int>(100,20); // int version
You can use the templatized type, T, inside the template function

## Slide 262
Template classes
Don’t want to write the same class many times for different types?
Templates allow class to be parameterized with a type(s) too.
template <typename T>
class Square
{
T operator() (T x) { return x*x; }
};
Square<int> f_int();
int value = f_int(10);

## Slide 263
C++11 defines a function template
C++ function objects can be stored in the templated class std::function. The following header defines the class std::function
#include <functional>
We can define a C++ function object (e.g. functor) and then store it in the tempated class std::function
struct Functor
{
int operator() (int x) { return x*x; }
};
std::function<int (int)> square(Functor());

## Slide 264
C++ function template: example 1
The header <functional> just defines the template std::function. This can be used to warp standard functions or function objects, e.g.:
int foo(int x) { return x; } // standard function
std::function<int (int)> foo_wrapper(foo);
struct Foo // function object
{
void operator()(int x) {return x;}
};
std::function<int (int)> foo_functor(Foo());
foo_functor and foo_wrapper are basically the same but one is using a standard C like function, while the other is using a function object

## Slide 265
C++ function template: example 2
What is the point of function objects? Well they can of course contain local state, which functions cannot, they can also contain member functions and so on. A silly example might be:
struct Foo // function object
{
int y_;
Foo() : y_(100) {}
void operator()(int x) { return x+100; }
};
std::function<int (int)> add100(Foo());
// function that adds 100 to its argument
Notes: 265

## Slide 266
Python for C programmers
Appendix E

## Slide 267
Python 101
Python is an interpreted language, and so doesn’t need to be compiled
Python is often used as a language to glue other parts of your application together – with OpenCL this is great as the host code is fast to write and the heavy computation is done on your accelerator
Run your code as:
  python file.py
No curly braces – indent consistently to define blocks of code
Print to stdout with print – it will try it’s best to format variables:
print ‘a =‘, a, ‘and b =‘, b

## Slide 268
Comments, variables and includes
A comment is prefixed with the hash
# this is a comment
Initilize variables as you go – no need for a type
N = 1024
x = 5.23
my_string = 'hello world'
Use single or double quotes for strings
'this is the same'
"as this"
"no need to escape 'opposite' quotes!"
Also use three quotes ''' or """ for multiline strings without escaping anything!
Include additional modules and libraries with
import sys

## Slide 269
Conditionals
if n == 1:
print ‘n was 1’
elif n == 2 or n == 3:
print ‘n was 2 or 3’
else:
print ‘n was’, n

## Slide 270
Loops
# loop from 0 to 1023
for i in range(1024):
print i
# iterate through an array
for x in my_array:
x += 1
# same as the first one
while i < 1024:
print i
i += 1

## Slide 271
Functions and classes
Define a function with the def keyword
def func(arg):
You don’t specify the types or return arguments
  you just return what you like
Define a class with the class keyword
class name:
Classes contain function definitions and variables
  These are both called attributes

## Slide 272
More about classes
There is a lot more about classes e.g. inheritance
Python is an object-oriented language
A small example from the python tutorial:
class Complex:
def __init__(self, realpart, imagpart):
self.r = realpart
self.i = imagpart
Initilize an instance of the class with:
x = Complex(3.0, -4.5)

## Slide 273
Python has functional programming elements
Filter
filter(function, sequence)
  Returns a list from sequence which function returns true
Map
map(function, sequence)
  Applies the function to each element in the sequence
Reduce
reduce(function, sequence)
  Applies binary function with first two in sequence, then with the result with third, etc.

## Slide 274
Python has functional programming elements
List comprehensions
squares = [x*x for x in range(10)]
# squares = [0, 1, 4, 9, 16, etc]
Zip
zip(list1, list2)
  Creates a list of tuples, where the ith tuple consists of the ith elements of each list
Generators
  Lazy generation of lists
  Either:
    Replace [] with () in list comprehensions to use as expression, i.e. to pass to another function
    Use the yield keyword instead of return in a function which builds and returns a list

## Slide 275
Further information:
There is lots more to python, this is just a flavor of the language to help you understand the syntax in this course
The official python tutorial is much more complete:
  http://docs.python.org/2/tutorial/index.html
The python docs are really good too
  http://docs.python.org/2/library/index.html